## Slide 1: EECS 370 - Lecture 15
Exam Review
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link

## Slide 2: Exam stuff
Exam is on Thursday March 9th from 7-9pm.
  Room assignments on Piazza (post 2068).
What can you have?
  We’ll supply the ARMv8 quick reference card and a handout
    See post 2068 on Piazza for the handout
  You can bring an 8.5 by 11 sheet with notes (both sides fine)
  Calculator without wireless capability
    No storing stuff in it.
Topics?
  Through lecture 15
    Again, see the Piazza post for details.
  HW 1-3
  Programming assignments 1, 2a, 2l.
2

## Slide 3: Exam Advice
Read the first page of the midterm exam
Sign the honor pledge!
  No signature = no grade
Pay attention to time
  Don’t get stuck on a single problem
  Answer as many questions as possible

## Slide 4: Preparing for the Exam
Review the lecture notes
Go over old homework assignments
Go over old discussion examples
Skim through the book sections specified
Past exams w/solutions wuill be posted to course website
  Complete without looking at the solutions!
  Some topics are no longer relevant (e.g., MIPS ARMv7)

## Slide 5: Important Topics
Representing values in hardware
  Binary, octal, hexadecimal conversions
  2’s complement representation
  Floating point formats
Instruction sets
  Assembly code LEGv8/ LC2k: write & understand
  Converting to machine code
  Addressing modes for load/store instructions
  Conditional instructions

## Slide 6: Important Topics
Converting C to assembly and back
  Data alignment
  Basic statements
  Control flow constructs
Running programs
  Data organization (stack, heap, static, text)
  Stack frames, stack and frame pointers
  Object files: symbol table and relocation table
  Caller/callee-saved registers
  Compiler, linker, loader

## Slide 7: Important Topics
Logic gates, devices and basic state machines
  AND, OR, NOT, XOR, etc. gates
  Decoders, MUXes, ALUs, etc.
  Latches and flip-flops
  Next state and output logic (via control ROM)
Data path
  Single cycle, multi-cycle, pipeline
  CPI and performance computations
  Adding new instructions

## Slide 8: Review Questions
If a topic is not covered in this review, it does not imply that it is not important!

## Slide 9: Memory Layout
How many bytes does the C data structure require (assuming a 64-bit machine)?
    struct foo {
    double *w;
    char x;
    int y;
    char z[10];
    };
How could this structure be rewritten to reduce memory usage?
8 bytes
1 byte
4 bytes + 3 bytes for alignment
1 * 10 bytes
26 bytes + 6 for padding= 32 bytes

## Slide 10: Memory Layout
How many bytes does the C data structure require?
    struct foo {
    double *w;  8 bytes
    char x;  1 byte
    int y;  4 bytes + 3 bytes for alignment
    char z[10];  1 * 10 bytes
    };  26 bytes + 6 bytes padding = 32
How could this structure be rewritten to reduce memory usage?
    struct foo {
    double *w;  8 bytes
    int y;  4 bytes
    char z[10];  1 * 10 bytes
    char x;  1 byte
    };  23 bytes + 1 byte padding = 24

## Slide 11: Big Endian vs. Little Endian
Endian-ness: ordering of bytes within a word
  Little - increasing numeric significance with increasing memory addresses
  Big – The opposite, most significant byte first
  The Internet is big endian, x86 is little endian, LEG and ARMv8 can switch
Notes: Endian – form Swift’s Lilliput
Lilliputians open boiled eggs at the smaller end. Their enemies are Big-Endians living in Blefuscu.

## Slide 12: Example Code Sequence
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
0x02
0x03
0xFF
0x05
100
101
102
103
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0xC2
0x06
0xFF
0xE5
104
105
106
107
We shown the registers as blank. What do they actually contain before we run the snippet of code
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
STURB X4, [X5, #102]
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 13: Example Code Sequence
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
STURB X4, [X5, #102]
0x02
0x03
0xFF
0x05
100
101
102
103
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0xC2
0x06
0xFF
0xE5
104
105
106
107
0xE5FF06C205FF0302
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 14: Example Code Sequence
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
0x02
0x03
0xFF
0x05
100
101
102
103
0x00000000000000FF
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0xC2
0x06
0xFF
0xE5
104
105
106
107
0xE5FF06C205FF0302
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
STURB X4, [X5, #102]
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 15: Example Code Sequence
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
0xFF
0x00
0x00
0x00
100
101
102
103
0x00000000000000FF
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0x00
0x00
0x00
0x00
104
105
106
107
0xE5FF06C205FF0302
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
STURB X4, [X5, #102]
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 16: Example Code Sequence
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
0xFF
0x00
0x02
0x00
100
101
102
103
0x00000000000000FF
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0x00
0x00
0x00
0x00
104
105
106
107
0xE5FF06C205FF0302
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
STURB X4, [X5, #102]
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 17: Example Code Sequence (2)
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
LDURSW X4, [X5, #102]
0x02
0x03
0xFF
0x05
100
101
102
103
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0xC2
0x06
0xFF
0xE5
104
105
106
107
We shown the registers as blank. What do they actually contain before we run the snippet of code
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 18: Example Code Sequence (2)
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
LDURSW X4, [X5, #102]
0x02
0x03
0xFF
0x05
100
101
102
103
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0xC2
0x06
0xFF
0xE5
104
105
106
107
0xE5FF06C205FF0302
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 19: Example Code Sequence (2)
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
0x02
0x03
0xFF
0x05
100
101
102
103
0x00000000000000FF
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0xC2
0x06
0xFF
0xE5
104
105
106
107
0xE5FF06C205FF0302
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
LDURSW X4, [X5, #102]
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 20: Example Code Sequence (2)
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
0xFF
0x00
0x00
0x00
100
101
102
103
0x00000000000000FF
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0x00
0x00
0x00
0x00
104
105
106
107
0xE5FF06C205FF0302
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
LDURSW X4, [X5, #102]
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 21: Example Code Sequence (2)
What is the final state of memory once you execute the following instruction sequence? (assume X5 has the value of 0)
0xFF
0x00
0x00
0x00
100
101
102
103
0x00000000000000FF
X3
X4
register file
Memory (each location is 1 byte)
ARM ISA
little endian
0x00
0x00
0x00
0x00
104
105
106
107
0x0000000000000000
LDUR X4, [X5, #100]
LDURB X3, [X5, #102]
STUR X3, [X5, #100]
LDURSW X4, [X5, #102]
Notes: Lc2K – bendian doesn’t matter because each location is a word
little endian / big endian
little endian: intel, arm
big-endian: motorola, old sun/java, networks, powerPc
bi-endian: mips
gulliver

## Slide 22: Load Instruction Sizes
How much data is retrieved from memory at the given address?
LDUR X3, [X4, #1000]
  Load (unscaled) to register—retrieve a double word (64 bits) from address (X4+1000)
LDURH X3, [X4, #1000]
  Load halfword (16 bits) from address (X4+1000) to the low 16 bit in X3—top 48 bits of X3 are set zero
LDURB X3, [X4, #1000]
  Load byte (8 bits) from address (X4+1000) and put in the low 8 bits of X3—zero extend the destination register X3 (top 56 bits)
What about loading words?
LDURSW X3, [X4, #1000]
  retrieve a word (32 bits) from address (X4+1000) and put in lower half of X3—top 32 bits of X3 are sign extended
  the most significant bit of the word at address (X4+1000) is copied into the top 32 bits of X3
ARM ISA
Notes: LDURSW is the only sign extended load.

## Slide 23: LEG Pseudos
MOV X3, X4
Expanded to: LSL X3, X4, #0 // many other possibilities
CMP X9, X10 // compare X9 to X10 and set condition code
Expands to: SUBS XZR, X9, X10 // use X9 − X10 to set condition codes
  We allow writes to XZR (X31) to set condition codes—the result is discarded
  Immediates allowed

## Slide 24: IEEE Floating point format (single precision)
Sign bit: (0 is positive, 1 is negative)
Significand: (also called the mantissa; stores the 23 most significant bits after the decimal point)
Exponent: used biased base 127 encoding
  Add 127 to the value of the exponent to encode:
  -127  00000000 1  10000000
  -126  00000001 2  10000001
  … …
  0  01111111 128  11111111
How do you represent zero ? Special convention:
  Exponent: -127 (all zeroes ), Significand 0 (all zeroes), Sign + or -

## Slide 25: IEEE 754 Floating Point
What is the value, in binary, of the following IEEE 754-encoded floating-point number?
What is the value, in decimal, for the same number?
1.101 x 20 1.625 x 20
0
01111111
10100000000000000000000

## Slide 26: Symbol Table & Relocation Table
File main.c
1: int r;
2: extern int x;
3: extern void foobar();
4: void main(int a) {
5: reference to x
6: reference to r
7: foobar();
8: return; }
File foobar.c
1: int x;
2: int y;
3: void foobar() {
4: int t;
5: reference to x
6: reference to y
7: reference to t
8: return; }
What symbols appear in the symbol tables?
What instructions appear in the relocation tables?
Symbol Table:
r, x, foobar, main
Relocation Table:
5, 6, 7
Symbol Table:
x, y, foobar
Relocation Table:
5, 6

## Slide 27: Assigning Variables to Memory Spaces
int z;
static float q;
int foo() {
int a, b, c;
static int d;
a = 1;
b = bar(a);
c = a + b;
char *s;
s = malloc(10);
printf(s);
return;
}
z = data
q = data
a,b,c = stack
d = data
s = stack;
t = stack,
*s = heap
s = stack

## Slide 28: Q for a D flip-flop?
Data
Clock
Q

## Slide 29: Datapath
We’ve covered three datapaths
  Single-cycle
  Multi-cycle
  Pipeline

## Slide 30: Data path Performance Questions
Consider an LC2K program which consists of:
  20 loads
  25 stores
  15 beqs
  10 nors
  30 adds
What would be the execution time for:
  Our single-cycle datapath with a clock period of 100ns
  Our multi-cycle datapath with a clock period of 20ns
  Our pipelined datapath with a clock period of 25ns (with no stalls).
10,000 ns (10 s)
8,400 ns (8.4 s)
2,600 ns (2.6 s)
Notes: 104*25=2600

## Slide 31: Multicycle Datapath
Consider the above LC-2K multicycle datapath covered
in lecture. We want to provide hardware support for a
new instruction:
destReg = regA++ + regB
List any new hardware components that need to be introduced to the LC-2K datapath to directly support the new instruction.
List any new control signals that need to be introduced to the LC-2K control to provide support for the new instruction.

## Slide 32
Regen
IRen
PC
Memory
Register
file
M
U
X
M
U
X
M
U
X
Sign extend
A
L
U
R/W
En
En
M
U
X
M
U
X
Instruction Reg
Control
addr
data
En
En
PCen
MUXaddr
Memen
Memr/w
MUXdest
MUXrdata
MUXalu2
MUXalu1
ALUop
1
0
ALU result

## Slide 33: Multicycle Datapath – F05E2 (Q. II.C cont.)
Give a cycle by cycle description of the LC-2K operation when executing the new instruction. For each cycle, give the following information: Single-sentence description of what the cycle is about,
and Register updates. Use as few cycles as possible.
Cycle 1 Fetch instruction
Instruction Register = new instruction
ALU Result = PC + 1
Cycle 2 Decode instruction and read registers
PC = PC + 1
Finish the rest

## Slide 34: Multicycle Datapath – F05E2 (Q. II.C cont.)
Cycle 1 Fetch instruction
Instruction Register = new instruction
ALU Result = PC + 1
Cycle 2 Decode instruction and read registers
PC = PC + 1

## Slide 35: Question II.C 3 - answer
Cycle 1 // Fetch instruction
Instruction Register = new instruction
ALU Result = PC + 1
Cycle 2 // Decode instruction and read registers
PC = PC + 1
Cycle 3 // Add regA and regB
ALUResult = regA + regB
Cycle 4 // Store ALUResult to destR
RegisterFile[destR] = ALUResult
// Add regA and 1
ALUResult = regA + 1
Cycle 5 // Store ALUResult to regA
RegisterFile[regA] = ALUResult
destReg = regA++ + regB 
destReg = regA++ + regB
regA = regA + 1

## Slide 36
Regen
IRen
PC
Memory
Register
file
M
U
X
M
U
X
M
U
X
Sign extend
A
L
U
R/W
En
En
M
U
X
M
U
X
Instruction Reg
Control
addr
data
En
En
PCen
MUXaddr
Memen
Memr/w
MUXdest
MUXrdata
MUXalu2
MUXalu1
ALUop
1
0
ALU result

## Slide 37: Question II.C 1 and 2 - answers
1. Add a entry to the MUX connecting to the register
write address port to the register file, making it 3-1 MUX.
Connect the instruction_reg[21:19] (the regA field) to the
new MUX input.
2. A second control bit is required for the new MUX.

## Slide 38: Pipelining
Say you have the following LC2K program:
  beq 1 0 0 //not taken
  add 1 1 1
  lw 1 2 15
How long would it take for that program to finish the lw on our 5-stage pipeline with “detect and stall” used to resolve data and control hazards?
Cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12

## Slide 39: Pipelining
Say you have the following LC2K program:
  beq 1 0 0 //not taken
  add 1 1 1
  lw 1 2 15
How long would it take for that program to finish the lw on our 5-stage pipeline with “detect and stall” used to resolve data and control hazards?
Cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
beq | F | D | X | M | W |  |  |  |  |  |  | 
add |  |  |  |  | F | D | X | M | W |  |  | 
lw |  |  |  |  |  | F | D* | D* | D | X | M | W