## Slide 1: EECS 370 - Lecture 17
Cache Introduction
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link

## Slide 2: Announcements
P3 published
  Checkpoint due Thursday
    5% of project – have pipeline working without data hazards or branches
Midterm scores should be available later this week
HW 4 posted, due next Monday

## Slide 3: Resources
Pipelining not clicking? Try playing with the "Pipeline Simulator" under "Resources" on the website
  https://vhosts.eecs.umich.edu/370simulators/pipeline/simulator.html
  Several pre-written programs you can step through to understand what's going on
  Note that the project pipeline is slightly different

## Slide 4: Project Pipeline
Design is largely the same as lecture, except no "internal forwarding" through the register file
  I.e. we need to explicitly forward from a new pipeline register WBEND if source instruction is in WB while dependent is in Decode

## Slide 5: Project 3 Pipeline
PC
Inst
mem
Register
file
M
U
X
Sign extend
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/ID
ID/EX
EX/Mem
Mem/WB
M
U
X
0-2
16-18
WBEND
M
U
X

## Slide 6: LC2K Pipeline Summary
Data hazards
  Hazard exists if producer-consumer of a register is within a certain "window size"
  Lecture 5-stage pipeline: 2 instruction window
  Project 5-stage pipeline: 3 instruction window
  Detect and stall – insert enough noops to separate producer and consumer
  Detect and forward
    For 5-stage pipeline, handles all cases except LW followed by dependent (need 1 noop)
Control hazards
  Detect and stall – insert noops after IF stage
    3 noops needed in our design
  Detect and squash – only insert noops if we're wrong
    Again, 3 needed in our design
Fetch
PC read
Decode
Execute
Need register values
Memory
Branches resolved
WB
Register values produced

## Slide 7: EECS 370 Overview
Part I: Software
Part II: Processor Design
Part III: Memory Design
  Starting with: caches
If we judge a component's value by how much space it takes up on a chip (not a terrible heuristic), caches are very valuable
Cache

## Slide 8: Cache Aware vs Non-Aware Code
Live Poll + Q&A: slido.com #eecs370
Notes: Code on the left ends up performing better because cache ends up storing sequential memory address together (we'll understand this better in the coming weeks)

## Slide 9: Memory
So far, we have discussed two structures that hold data:
  Register file (little array of words)
  Memory (bigger array of words)
How do we build this?
  We need a lot of memory: 218 for LC2K, a lot more for ARM
  Bunch of flip-flops? Not practical – too many transistors, would be huge and power hungry
  Other, clever ways of storing bits

## Slide 10: Option 1: SRAM
Each bit is made of 6 transistors
Volatile: need constant power to keep data
Fast: ~1 ns read time
Still rather large and expensive
  ~$5 per megabyte
Impractical to scale up to GBs needed for modern systems
Replace cost with how much we can fit on chip

## Slide 11: Option 2: DRAM
Each bit is made of a transistor and capacitor
Volatile: need constant power to keep data
Slower: ~50 ns access time
  Must stall for dozens of cycles on each memory load
Less expensive for SRAM
  ~$0.004 per megabyte
  We can put up to ~16 GB in current machines
  Good for LC2K or 32-bit systems
  But not for 64-bit systems

## Slide 12: Option 3: Disks
Hard-drives store bits as magnetic charges on spinning disks
  Non-volatile – holds information even when no power is supplied
  Obnoxiously slow compared to digital logic: 3,000,000 ns access time
Recently, solid-state drives have replaced spinning disks with logic gates replacing mechanical systems
  Also non-volatile
  Much better speeds (3,000,000 ns), but still to slow to keep up with processor
Cheap!
  SSDs cost $0.0001 per megabyte
  Scale up to terabytes – practical for modern computing

## Slide 13: Memory Goals
Fast: Ideally run at processor clock speed
  1 ns access
Cheap: Ideally free
  Not more expensive than rest of system
DRAM, hard-drives and SSDs are too slow
SRAM is too expensive
How to get best properties of multiple memory technologies?

## Slide 14: Memory Hierarchy
Key observation: we only need to access a small amount of data at a time
Let's use a small array of SRAM to hold data we need now
  Call this the cache
  Able to keep up with processor
  Small (~Kilobytes), so it should be relatively cheap
Use a large amount of DRAM for main memory
  Can scale up to ~Gigabytes in size
Everything else, store on disk
  Virtual Memory
Won't end up building 264 of anything
  Won't be needed in typical programs
  Virtual memory (discussed in a couple weeks) will make memory look larger than it is

## Slide 15: Cache Analogy
Studying in the library
  Option 1: Every time you grab another book, return current book to shelf and get a new book from shelf
    Latency = 5 minutes
  Option 2: Keep 10 commonly-used books on shelf above desk
    Latency = 1 minute
  Option 3: Keep 3 books open on different locations on desk
    Latency = 10 seconds

## Slide 16
Memory
Regs
Small
Big
Fast
Slow
Caches
Managed explicitly by programmer / compiler
Managed transparently by hardware
Memory Hiearchy

## Slide 17
Pipeline
Memory
1 op / 100 cycles
Pipeline
Memory
1 op / 100 cycles
Cache
1 op / 1 cycle
ld
ld
ld
Caches - Overview

## Slide 18: Function of the Cache
The cache holds the data we think is most likely to be referenced
  The more often the data we want is in the fast cache, the lower our average memory access latency is
  How do we decide what the most likely accessed memory locations are?

## Slide 19: The simplest cache
Memory
Only worry about load instructions for now
Word-addressable address space
Consists of a single, word-size storage location to remember last loaded value
Data
Pipeline

## Slide 20: The simplest cache
Whenever memory returns data, store it in the cache
We’ll also need to know what address this data corresponds to
  Store that as “tag”
Also include a “valid” status bit
Tag | Data | Status
0x09 | 17 | Valid
Pipeline
Memory
mem[0x09]=17
ld 0x09

## Slide 21: The simplest cache
Next memory access, first check if the tag matches address
  Yes? Return cache data
  No? Go to memory as before
Tag | Data | Status
0x09 | 17 | Valid
Pipeline
ld 0x09
mem[0x09]=17
Memory

## Slide 22: Definitions
Hit: when data for a memory access is found in the cache
Miss: when data for a memory access is not found in the cache
Hit/Miss rate: percentage of memory accesses that hit/miss in the cache

## Slide 23: Example Problem
Assume the following:
  Cache has 1 cycle access time
  If data is not found in cache, main memory is then accessed instead
  Main memory has 100 cycle access time
If we have a 90% hit rate in the cache, what is the average memory latency?
Poll: Average access time?
1 + 0.1 * ( 100 ) = 211
Live Poll + Q&A: slido.com #eecs370

## Slide 24: Scaling Up
Of course, we don't just access one memory location
What if we access many memory locations, and cache isn't large enough to hold all of them?
How do we choose what to keep in the cache?
  How does hardware predict what's most likely to be needed soon?
Answer: locality
  Temporal locality
  Spatial locality

## Slide 25: Temporal Locality
Temporal locality: if a given memory location is referenced now, it will probably be used again in the near future
  Why? Take a look at code you've written. You tend to use a variable multiple times
  Corollary: if you haven't used a variable in a while, you probably won't need it very soon either
Hardware should take advantage of this by:
  Placing items we just accessed in the cache
  When we need to evict something, evict whatever data was least recently used (LRU)

## Slide 26: A Very Simple Memory System
74
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
tag data
R0
R1
R2
R3
Memory
2 cache lines
4 bit tag field
1 byte block
V
V

## Slide 27: A Very Simple Memory System
74
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
tag data
R0
R1
R2
R3
Memory
Is it in the cache?
No valid tags
This is a
Cache miss
Allocate: address  tag
Mem[1]  block
1
110
0
0
1

## Slide 28: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
tag data
R0
R1
R2
R3
Memory
110
lru
Misses: 1
Hits: 0
110
74
1
0

## Slide 29: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
tag data
R0
R1
R2
R3
Memory
110
Misses: 1
Hits: 0
110
lru
74
Check tags: 5  1
Cache Miss
1
0
1
150
5
Tag comparison uses hardware called "content-addressable memory (CAM)"

## Slide 30: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 0
110
lru
74
150
1
1

## Slide 31: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 0
110
150
lru
74
Check tags: 1  5,
but 1 = 1 (HIT!)
1
1

## Slide 32: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 1
110
150
lru
74
110
1
1

## Slide 33: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 1
110
150
lru
74
110
1
1

## Slide 34: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
5
tag data
R0
R1
R2
R3
Memory
110
150
Misses: 2
Hits: 1
110
150
lru
74
110
7  5 and 7  1
(MISS!)
170
170
1
1
7

## Slide 35: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
7
tag data
R0
R1
R2
R3
Memory
110
170
Misses: 3
Hits: 1
110
150
170
lru
74
1
1

## Slide 36: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
7
tag data
R0
R1
R2
R3
Memory
110
170
Misses: 3
Hits: 1
110
150
170
lru
74
7  1 and 7 = 7
(HIT!)
170
1
1

## Slide 37: A Very Simple Memory System
100
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ld R1  M[ 1 ]
Ld R2  M[ 5 ]
Ld R3  M[ 1 ]
Ld R3  M[ 7 ]
Ld R2  M[ 7 ]
Cache
Processor
1
7
tag data
R0
R1
R2
R3
Memory
110
170
Misses: 3
Hits: 2
110
170
170
lru
74
1
1

## Slide 38: Next time
Making our caches bigger and better
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah

## Slide 40: Calculating Average Access Latency
Average Latency:
Average latency for our example:
To improve latency, either:
  Improve memory access latency, or
  Improve cache access latency, or
  Improve cache hit rate

## Slide 41: Calculating Size
How many bits is used in cache?
  Storing data
    2 bytes of SRAM
  Calculate overhead (non-data)
    This cost is often forgotten for caches, but it drives up the cost of real designs!
    2 4-bit tags
    2 valid bits
What is the storage requirement
Poll: Which of the following would reduce tag overhead (as an overall percentage)? (select all that apply)
Increase number of cache entries
Decrease number of cache entries
Use smaller addresses
Store more data in each cache entry
Live Poll + Q&A: slido.com #eecs370

## Slide 42: How can we reduce overhead?
Have a smaller address
  Impractical, and caches are supposed to be micro-architectural
Cache bigger units than bytes
  Each block has a single tag, and blocks can be whatever size we choose.
1
7
tag data
110
170
lru
1
1

## Slide 43: Increasing Block Size
Case 1:
Block size: 1 bytes
0
6
V tag data (block)
74
160
1
1
74
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Memory
How many bits needed per tag?
= log2(number of blocks in memory) = log2(16)
= 4 bits
Overhead = (4+1) / 8 = 62.5%
Case 2:
Block size: 2 bytes
0
3
V tag data (block)
74
160
1
1
110
170
How many bits needed per tag?
= log2(number of blocks in memory) = log2(8)
= 3 bits
Overhead = (3+1) / 16 = 25%
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
1
1
2
2
3
3
4
4
5
5
6
6
7
7
Poll: What will the overhead of this cache be?
Live Poll + Q&A: slido.com #eecs370
Tag
(case 1)
Tag
(case 2)

## Slide 44: Figuring out the tag
If block size is N, what's the pattern for figuring out the tag from the address?
If block size is power of 2, then this is just everything except the bits of the address in binary!
E.g.
Remaining bits (block offset) tells us how far into the block the data is
74
110
120
130
140
150
160
170
180
190
200
210
220
230
240
250
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Memory
0
0
1
1
2
2
3
3
4
4
5
5
6
6
7
7
Tag
(case 2)
Poll: What's the pattern?
Live Poll + Q&A: slido.com #eecs370