## Slide 1: EECS 370 - Lecture 2
ISA and Binary
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link
Poll: Why is multiplying numbers by 100 easier than multiplying by 128?

## Slide 2: Unresolved questions from last time
"Is there a reason that most programming languages are open source but architectures IP?"
  Designing hardware is expensive!
  Anyone can write software: incentive to develop toolchains and share them with people
  Actually implementing a processor design takes millions of dollars. Mostly only specialized companies develop toolchains, and sell them to other companies for big $$$
  But that's gradually changing!
Remember, you can post questions on Slido, or fill out this "end of lecture" form:
Live Poll + Q&A: slido.com #eecs370

## Slide 3: Announcements
HW 0
  Posted on website, due Wednesday
P1
  Released soon
Setup clinic
  Friday
  Need help getting your debugger setup?
OH
  Going on now: see website->Google Calendar->Office Hours

## Slide 4: My Office Hours
2 types:
Group:
  In-person
  T/Th - 30 minutes right after class (3901 BBB)
  Prioritize group questions over individual debugging
  Starting this Thursday
Individual:
  Wednesday – 4:30-5:30
  Over Zoom (for now) – see website for link
  One-on-one: any questions welcome

## Slide 5: Extra Resources
Want more examples on binary? Two's complement?
  See "resources tab" on website
  Extra videos, review sheets

## Slide 6: Instruction Set Architecture (ISA) Design Lectures
Lecture 2: ISA - storage types, binary and addressing modes
Lecture 3 : LC2K
Lecture 4 : ARM
Lecture 5 : Converting C to assembly – basic blocks
Lecture 6 : Converting C to assembly – functions
Lecture 7 : Translation software; libraries, memory layout

## Slide 7: Basic Computer Model
You know from 280 that computers have "memory"
  Abstractly, a long array that holds values
Every piece of data in a running program lives at a numerical address in memory
  You can see the address in C by using the "&" operator
Most programs work by loading values from memory to the processor, operating on those values, and writing values back into memory

## Slide 8: Basic Memory Model
1st question in understanding how programs run on computers:
  How are values actually represented in memory?
Answer: binary

## Slide 9: Aside: Decimal and Binary
Humans represent numbers in base-10 (decimal) because we have 10 fingers (or "digits")
The nth digit corresponds to 10n
Computers are made of wires with either high or low voltages
Internally represents values in base-2 (binary) since it has "binary digits"
  (or bits for short)
In binary, the nth bit corresponds to 2n
Does Bart Simpson count in octal?
Collection of 8 bits is called a byte

## Slide 10: Aside: Hexadecimal
A bunch of 0s and 1s is hard to read for humans
  But translating to decimal and back is tricky
Solution: Bases that are a power of 2 are easy to translate between, since a fixed group of bits corresponds to one digit
In practice, base-16 or hexadecimal is used
  Digits 0-9, plus letters A-F to represent 10-16

## Slide 11: Aside: Hexadecimal
Every 4 bits corresponds to 1 hex digit (since 24=16)
(binary) 0b 0010 0101 1010 1011
(hexadecimal)0x 2 5 A B
0x25AB
Live Poll + Q&A: slido.com #eecs370
Represent binary using 0b. Hex using 0x. If not specified, it's decimal

## Slide 12: Operating on Binary Values
All values are stored in binary, even when you specify the number in decimal
It is often convenient to treat values as sequences of bits, rather than values
  You will need to do this in P1a
C provides "bitwise operators" to do this
  Shift ("<<" and ">>")
  Bitwise boolean ("&", "|", "^", and "~")

## Slide 13: Shift Operators
Shift a value x bits to the left via "<<"
Inserts "x" zeros to the right (least significant)
E.g.
int a = 60;
int s = a << 2;

## Slide 14: Shift Operators
Shift a value x bits to the left via "<<"
Inserts "x" zeros to the right (least significant)
E.g.
int a = 60; // 0b0011_1100
int s = a << 2; // 0b1111_0000
"a" is still 60, "s" is 240
Same idea for ">>", but to the right
shifting to the left in decimal multiplying by
shifting to the left in binary multiplying by

## Slide 15: Bitwise operations
Bitwise operations apply a Boolean operation on each bit of a value (or each pair of bits across two values)
int a = 60; // 0b0011_1100
int b = 13; // 0b0000_1101
int o = a | b;

## Slide 16: Bitwise operations
Bitwise operations apply a Boolean operation on each bit of a value (or each pair of bits across two values)
int a = 60; // 0b0011_1100
int b = 13; // 0b0000_1101
int o = a | b; // 0b0011_1101
"a" and "b" are the same, "o" is 61
& – and | – or ^ – xor ~ – not
Very different from Boolean &&, ||, etc
  Why?

## Slide 17: Different Data Types
How does memory distinguish between different data types?
  E.g. int, int *, char, float, double
It doesn't! It's all just 0s and 1s!
We'll see how to encode each of these later
Exact length depends on architectures

## Slide 18: Minimum Datatype Sizzes
Type | Minimum size (bits)
char | 8
int | 16
long int | 32
float | 32
double | 64

## Slide 19: Where do ISAs come into the game ?
MICROARCHITECTURE (Hardware implementation of the ISA) - Intel Core i9/i7/i5 implements the x86 ISA (desktop laptop) - Apple A9 implements the ARM v8-A ISA (iPhone)
ARCHITECTURE – a.k.a. ISA (Instruction Set Architecture) - Platform-specific - a limited set of assembly language commands "understood" by hardware (e.g. ADD, LOAD, STORE, RET)
Circuits
Devices
Compilers
Application software
The hw/sw
divide

## Slide 20: How is Assembly Different from C/C++?
C/C++: string multiple operations & operands in one statement:
x = a + b + c - d
In assembly, you can
  only specify one of a fixed number of operations per statement, and
  have a fixed number of operands per statement
  ADD r1, r2, r3 // equivalent to r1 = r2 + r3
Complex Instruction Set Computing (CISC) ISAs focus on having many, complex instructions to make programming easier
  E.g. x86, not discussed in this class
Reduced Instruction Set Computing (RISC) ISAs focus on having fewer, simpler instructions to ease hardware design
  E.g. LC2K, ARM (sorta), primary focus of this class

## Slide 21: How is Assembly Different from C/C++?
C/C++ instructions operate on variables
  e.g.
  x = i+j;
  Practically unlimited
Assembly instructions operate on memory locations or registers
  e.g.
  add r1, r2, r3
  ld r1, 0x1000
  Registers are basically a small number (~8-32) of fixed-length, hardware variables that have simple names like "r5"

## Slide 22: Example Architectures
ARMv8—LEGv8 subset from P+H text book
  32 registers (X0 – X31)
  64 bits in each register
  Some have special uses e.g. X31 is always 0—XZR
Intel x86 (not discussed much in this class)
  4 general purpose registers (eax, ebx, ecx, edx) 32 bits
  Special registers: 3 pointer registers (si,di,ip), 4 segment (cs,ds,ss,es),
  2 stack (sp, bp), status register (flags)
LC2K (simple architecture made up for this class)
  8 registers, 32 bits each

## Slide 23: How is Assembly Different from C/C++?
C/C++: next line of code is executed until you get to:
  function call
  return statement
  if statement or for/while loop
  etc
Assembly: a program counter (PC) keeps track of which memory address has the next instruction, gets incremented until
  a "branch" or "jump" instruction
    Used to change control flow (more later)

## Slide 24: Traditional (von Neumann) Architecture
We're used to thinking about program code and data being separate
But in practice, both are stored in the same memory
  That's why things like "function pointers" in C/C++ work
This is the basis of the von Neumann Architecture

## Slide 25: Traditional (von Neumann) Architecture
Here’s the (endless) loop that hardware repeats forever:
Fetch—get next instruction–use PC to find where it is in memory and place it in instruction register (IR)
  PC is changed to “point” to the next instruction in the program
Decode—control logic examines the contents of the IR to decide what instruction it should perform
Execute—the outcome of the decoding process dictates
  an arithmetic or logical operation on data
  an access to data in the same memory as the instructions
  OR a change to the contents of the PC

## Slide 26: (Simplified) System Organization
Memory
Registers
+
32 x 64 bits
CPU
Gigabytes to Terabytes
Load
Store
ALU
Address FFFF…
Address 0000
X0 | 0
X1 | 7
X2 | -3
0102
Program counter
0102
ADD X0, X1, X2
Address 0102
ADD X0, X1, X2
SUB X1, X2, X0
Let's execute this short program:

## Slide 27: (Simplified) System Organization
Memory
Registers
+
32 x 64 bits
CPU
Gigabytes to Terabytes
Load
Store
ALU
Address FFFF…
Address 0000
X0 | 4
X1 | 7
X2 | -3
0103
Program counter
0103
SUB X1, X2, X0
Address 0103
ADD X0, X1, X2
SUB X1, X2, X0
Let's execute this short program:

## Slide 28: (Simplified) System Organization
Memory
Registers
+
32 x 64 bits
CPU
Gigabytes to Terabytes
Load
Store
ALU
Address FFFF…
Address 0000
X0 | 4
X1 | -7
X2 | -3
0104
Program counter
ADD X0, X1, X2
SUB X1, X2, X0
Let's execute this short program:

## Slide 29: Assembly Code – ARM Example
What are the contents of the registers after executing the given assembly code (destination register is listed first in ARM)?
ARM v8 ISA
Poll: What are the final contents of X1,X2, and X3?
ADD X3, X1, X2
ADDI X3, X3, #3
SUB X2, X3, X1
(1) ADD X3, X1, X2
(2) ADDI X3, X3, #3
25
X1
-4
X2
57
X3
Program:
Initial
register file:
opcode d s1 s2imm
25
X1
-4
X2
57
X3
25
X1
-4
X2
21
X3
25
X1
-4
X2
24
X3
25
X1
-1
X2
24
X3
(3) SUB X2, X3, X1
ADDI means "add immediate", the last field is a literal value, not a register index
Live Poll + Q&A: slido.com #eecs370

## Slide 30: How is Assembly Different from C/C++?
No data types in assembly
Everything is 0s and 1s: up to the programmer to interpret whether these bits should be interpreted as ints, bools, chars… or even instructions themselves!
char c = 'a';
c++; // c is now 'b'
// results in the same assembly as
int x = 97;
x++; // c is now 98

## Slide 31: How is Assembly Different from C/C++?
  1000011 could be interpreted as:
    Signed number: -61
    Unsigned number: 67
    A float: 9.38e-44
    A character: 'C'
    LC2K Instruction: 'add 0 0 3'
How did I get these?

## Slide 32: Representing Values in Hardware
Unsigned integers represented as we've seen
Chars are represented as ASCII values
  e.g. 'a' -> 97, 'b' -> 98, '#' -> 35
What about negative numbers?
Fractional numbers?

## Slide 33: Negative Numbers
There are many ways we could represent negative numbers
Because it will eventually make our hardware simpler, the most common representation is 2's complement
2
Hey, Good-Looking!
No, not 2's compliment!

## Slide 34: Two’s Complement Representation
Recall that 1101 in binary is 13 in decimal.
2’s complement numbers are very similar to unsigned binary numbers.
  The only difference is that the first number is now negative.
1 1 0 1 = -8 + 4 + 1= -3
-23 22 21 20
1 1 0 1 = 8 + 4 + 1= 13
23 22 21 20
Live Poll + Q&A: slido.com #eecs370

## Slide 35: Fun with 2's Complement Numbers
What is the range of representation of a 4-bit 2’s complement number?
  [-8, 7] (corresponding to 1000 and 0111)
What is the range of representation of an n-bit 2’s complement number?
  [-2(n-1), 2(n-1) - 1]
Useful trick: You can negate a 2’s complement number by inverting all the bits and adding 1.
  5 is represented as 0101
  Negate each bit: 1010
  Add 1: 1011 = -8 + 2 + 1 = -5

## Slide 36: What about fractional numbers?
One idea: fixed point notation
  Have some bits represent numbers before decimal point, some bits represent numbers after decimal point
Better idea: floating point notation
  Inspired by scientific notation (e.g. 1.3*10e-3)
  Allows for larger range of numbers
  We'll come back to this in a few weeks

## Slide 37: Encoding Instructions
So binary numbers can represent signed and unsigned numbers, chars, and fractional numbers
But they must also represent instructions themselves!
  After all, memory is just a collection of 1s and 0s
We need a way of encoding instructions in order to store them in memory

## Slide 38: Software program to machine code
Example ISA
(simplified)

## Slide 39: Assembly Instruction Encoding
Since the EDSAC (1949) almost all computers stored program instructions the same way they store data.
Each instruction is encoded as a number
This is the number stored in memory (in binary)!
011011010011001 = 20 + 23 + 24 + 27 + 29 + 210 + 212 + 213
= 13977
Poll: How many different "operation codes" could be supported by this ISA? How many registers?
Example ISA
(simplified)
Live Poll + Q&A: slido.com #eecs370

## Slide 40: Next Time
Finish Up ISAs
LC2K details
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah
Live Poll + Q&A: slido.com #eecs370