## Slide 1: EECS 370 - Lecture 21
Classifying Cache Misses
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link

## Slide 2: Announcements
P4
  Last project!
  Due Thu (4/13)
HW 6
  Last homework!
  Due Monday (4/17)
Final exam
  …Last exam!
  Thu (4/20) @ 10:30 am

## Slide 3: Announcements
Special topics lecture on Thursday (not covered in exam)

## Slide 4: Classifying Cache Misses
Cache misses happen for 3* reasons
  The 3C's of Cache misses:
Compulsory miss
  We've never accessed this data before
Capacity miss
  Cache is not large enough to hold all the data
  May have been avoided if we used a bigger cache
Conflict miss
  Cache is large enough to hold data, but was replaced due to overly restrictive associativity
  May have been avoided if we used a higher-associative cache
*On multi-core systems, there's a 4th C – take EECS 470/570 to learn more

## Slide 5: Classifying Cache Misses
Scenario: run given program on system with N-way cache of size M
  Identify each miss
We can classify each miss in a program by simulating on 3 different caches
  If miss still occurs in cache where size >= memory size: compulsory miss
  Else, if miss occurs in fully associative cache of size M: capacity miss
  Else, if miss occurs in N-way cache of size M (original cache): conflict miss

## Slide 6: 3C's Sample Problem
Consider a cache with the following configuration: write-allocate, total size is 64 bytes, block size is 16 bytes, and 2-way associative. The memory address size is 16 bits and byte-addressable. The replacement policy is LRU. The cache is empty at the start.
For the following memory accesses, indicate whether the reference is a hit or miss, and the type of a miss (compulsory, conflict, capacity)

## Slide 7: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 |  |  |  | 
0x14 |  |  |  | 
0x27 |  |  |  | 
0x08 |  |  |  | 
0x38 |  |  |  | 
0x4A |  |  |  | 
0x18 |  |  |  | 
0x27 |  |  |  | 
0x0F |  |  |  | 
0x40 |  |  |  | 
64 bytes total, 16 byte blocks, 2-way, 2 sets
Live Poll + Q&A: slido.com #eecs370

## Slide 8: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 | M |  |  | Compulsory
0x14 | M |  |  | Compulsory
0x27 | M |  |  | Compulsory
0x08 | H |  |  | 
0x38 | M |  |  | Compulsory
0x4A | M |  |  | Compulsory
0x18 | H |  |  | 
0x27 | H |  |  | 
0x0F | H |  |  | 
0x40 | H |  |  | 
64 bytes total, 16 byte blocks, 2-way, 2 sets
Poll: How many blocks will be in a 64 byte FA cache?
Live Poll + Q&A: slido.com #eecs370
Notes: 4 16-byte blocks

## Slide 9: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 | M | M |  | Compulsory
0x14 | M | M |  | Compulsory
0x27 | M | M |  | Compulsory
0x08 | H | H |  | 
0x38 | M | M |  | Compulsory
0x4A | M | M |  | Compulsory
0x18 | H | M |  | 
0x27 | H | M |  | 
0x0F | H | M |  | 
0x40 | H | H |  | 
64 bytes total, 16 byte blocks, 2-way, 2 sets

## Slide 10: 3 C’s Practice Problem – 3 C’s
Address | Infinite | FA | SA | 3Cs
0x00 | M | M | M | Compulsory
0x14 | M | M | M | Compulsory
0x27 | M | M | M | Compulsory
0x08 | H | H | H | ---
0x38 | M | M | M | Compulsory
0x4A | M | M | M | Compulsory
0x18 | H | M | H | ---
0x27 | H | M | M | Capacity
0x0F | H | M | M | Capacity
0x40 | H | H | M | Conflict
64 bytes total, 16 byte blocks, 2-way, 2 sets

## Slide 11: How to reduce cache misses
Compulsory miss
  Reduce by increasing cache block size
    Reduces total number of blocks for given cache size 
  Or by using prefetching (guess we'll need data based on previous memory patterns - discussed more in EECS 470)
Capacity miss
  Reduce by building a bigger cache
    Increase access latency 
Conflict miss
  Reduce by increasing associativity
    Increase access latency / overheads 

## Slide 12: Cache Performance
How does changing these parameters affect performance?
  Cache size
  Block size
  Associativity

## Slide 13: Cache Size
Cache size in the total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit & miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 14: Block size
Block size is the data that is associated with an address tag
  Sub-blocking: A block divided into multiple pieces (each with V bit)
    Can improve “write” performance
    Take 470 to learn more
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks
    likely-useless data transferred
    Extra bandwidth/energy consumed
Block size
hit rate

## Slide 15: Associativity
How many blocks can map to the same index (or set)?
Larger associativity
  lower miss rate, less variation among programs
  diminishing returns
Smaller associativity
  lower cost
  faster hit time
    Especially important for L1 caches
associativity
hit rate

## Slide 16: Extra Practice Problems
There are more problems than we’ll be able to cover today, but you are encouraged to work through these on your own
  They are good prep for the final exam

## Slide 17: Practice Problem 1: CPI with caches
The blaster application run on the LC2k with full data forwarding and all branches predicted not-taken has the following instruction frequencies:
45% R-type 20% Branches 15% Loads 20% Stores
In blaster, 40% of branches are taken and 50% of LWs are followed by an immediate use.
The I-cache has a miss rate of 3% and the D-cache has a miss rate of 6% (no overlapping of misses). On a miss, the main memory is accessed and has a latency of 100 ns. The clock frequency is 500 MHz.
Poll: What is the CPI increase over base (1) due to hazards?
Live Poll + Q&A: slido.com #eecs370

## Slide 18: Problem 1 Solution
The blaster application run on the LC2k with full data forwarding and all branches predicted not-taken has the following instruction frequencies:
45% R-type 20% Branches 15% Loads 20% Stores
In blaster, 40% of branches are taken and 50% of LWs are followed by an immediate use.
The I-cache has a miss rate of 3% and the D-cache has a miss rate of 6% (no overlapping of misses). On a miss, the main memory is accessed and has a latency of 100 ns. The clock frequency is 500 MHz.
What is the CPI of blaster on the LC2k?
Stalls per cache miss = 100 ns / 2ns = 50 cycles (500 Mhz ➜ 2ns cycle time)
CPI = 1 + data hazard stalls + control hazard stalls + icache stalls + dcache stalls
CPI = 1 + 0.15*0.50*1 + 0.20*0.40*3 + 1*0.03*50 + 0.35*0.06*50

## Slide 19: Practice Problem 2: Memory Usage
Say you have the following:
  A program that generates 2 Billion loads and 1 Billion stores, each 4 bytes in size.
  A cache with a 32-byte block which gets a 95% hit rate on that program.
How many bytes of memory would be read and written if:
  We had no cache?
  We had a write-though cache with a no-write allocate policy?
  We had a write-back cache with a write-allocate policy? (Assume 25% of all misses result in a dirty eviction)
Poll: How many bytes are read/written if we have no cache?

## Slide 20: Practice Problem 2: Memory Usage
Say you have the following:
  A program that generates 2 Billion loads and 1 Billion stores, each 4 bytes in size.
  A cache with a 32-byte block which gets a 95% hit rate on that program.
Let’s start with the no-cache case.
  All stores go to memory and are 4 bytes each
    Writes: 1 billion stores* 4 bytes = 4 billion bytes
  All loads go to memory and are 4 bytes each.
    Reads: 2 billion loads* 4 bytes = 8 billion bytes

## Slide 21: Practice Problem 2: Memory Usage
Say you have the following:
  A program that generates 2 Billion loads and 1 Billion stores, each 4 bytes in size.
  A cache with a 32-byte block which gets a 95% hit rate on that program.
Write-though, no allocate.
  All stores still go to memory and are still 4 bytes each.
    Writes: 1 billion stores* 4 bytes = 4 billion bytes
  Only loads that miss in the cache go to memory. But they read the full cache block.
    Reads: 2 billion loads* 0.05* 32 bytes = 3.2 billion bytes

## Slide 22: Practice Problem 2: Memory Usage
Say you have the following:
  A program that generates 2 Billion loads and 1 Billion stores, each 4 bytes in size.
  A cache with a 32-byte block which gets a 95% hit rate on that program.
Write-back, write-allocate (data reads)
  Store misses result in a cache block being read.
    Reads: 1 billion stores* 0.05* 32 bytes = 1.6 billion bytes
  Load misses result in a cache block being read.
    Reads: 2 billion loads* 0.05* 32 bytes = 3.2 billion bytes
  So that is 4.8 billion bytes of data read.

## Slide 23: Practice Problem 2: Memory Usage
Say you have the following:
  A program that generates 2 Billion loads and 1 Billion stores, each 4 bytes in size.
  A cache with a 32-byte block which gets a 95% hit rate on that program.
Write-back, write-allocate (data writes)
  Store misses result in dirty eviction 1/4 of the time.
    Reads: 1 billion stores* 0.05* 32 bytes*(.25) = 0.4 billion bytes
  Load misses result in a cache block being read.
    Reads: 2 billion loads* 0.05* 32 bytes*(.25) = 0.8 billion bytes

## Slide 24: Practice Problem 3: CPI w/ Caches 2
Given a 200 MHz processor with 8KB instruction and data caches and a with memory access latency of 20 cycles. Both caches are 2-way associative. A program running on this processor has a 95% icache hit rate and a 90% dcache hit rate. On average, 30% of the instructions are loads or stores. The CPI of this system, if caches were ideal would be 1.
Suppose you have 2 options for the next generation processor, which do you pick?
  Option 1: Double the clock frequency—assume this will increase your memory latency to 40 cycles. Also assume a base CPI of 1 can still be achieved after this change.
  Option 2: Double the size of your caches, this will increase the instruction cache hit rate to 98% and the data cache hit rate to 95%. Assume the hit latency is still 1 cycle.

## Slide 25: Practice Problem 3: Solution
Option 1: (double clock freq, base cycle time is 5 ns, so new cycle time is 2.5 ns)
  CPI = baseCPI + IcacheStallCPI + DcacheStallCPI
  CPI = 1.0 + 0.05*40 + 0.3*0.1*40 = 4.2
Execution time = 4.2 * Ninstrs * 2.5ns = 10.5ns * Ninstrs
Option 2 (icache/dcache miss rates lowered to 2% and 5%)
CPI = baseCPI + IcacheStallCPI + DcacheStallCPI
CPI = 1.0 + 0.02*20 + 0.3*0.05*20 = 1.7
Execution time = 1.7 * Ninstrs * 5ns = 8.5ns * Ninstrs
Therefore, Option 2 is the better choice

## Slide 26: Practice Problem 4: Guess that cache!
Similar to homework! Here is the series of address references (in hex) to a cache of size 512 bytes. You are asked to determine the configuration of the cache. Assume 12-bit addresses
0x310 – Miss
0x30f – Miss
0x510 – Miss
0x31f – Hit
0x72d – Miss
0x72f – Hit
0x320 – Miss
0x520 – Miss
0x720 - Miss
Block size: ?
Associativity: ?
Number of sets: ?

## Slide 27: Practice Problem 4: Guess that cache!
Here is the series of address references (in hex) to a cache of size 512 bytes. You are asked to determine the configuration of the cache. Assume 12-bit addresses
0x310 – Miss
0x30f – Miss
0x510 – Miss
0x31f – Hit
0x72d – Miss
0x72f – Hit
0x320 – Miss
0x520 – Miss
0x720 - Miss
Determine block size
First hit must be brought in by another miss
Take closest address: 0x310, so know block size must be at least 16 bytes so 0x31f brought in when 0x310 miss occurs
Now, is the block size larger? Know that 0x30f was a miss, thus 0x310 and 0x30f not in the same block. Thus, block size must be <= 16 bytes
Thus Block Size = 16 bytes

## Slide 28: Practice Problem 4: Guess that cache!
Here is the series of address references (in hex) to a cache of size 512 bytes. You are asked to determine the configuration of the cache. Assume 12-bit addresses
0x310 – Miss
0x30f – Miss
0x510 – Miss
0x31f – Hit
0x72d – Miss
0x72f – Hit
0x320 – Miss
0x520 – Miss
0x720 - Miss
Determine associativity
Assume direct mapped: 3-bit tag, 5-bit index, 4-bit offset.
If DM, 0x310 and 0x510 would both map to index 17,
Thus 0x31f could not be a hit. So, not direct mapped.
Assume 2-way associative: 4-bit tag, 4-bit index, 4-bit offset
This fixes the green accesses, and allows 0x31f to be a hit.
What about > 2-way associative?
Now we also know that 0x720 is a miss even though 3 accesses
earlier 0x72f was a hit, and thus it is in the cache. The intervening 2 accesses must kick it out, 0x320 and 0x520. Both go to set 2. If the associativity was > 2, then 0x720 would be a hit. So, must conclude that cache is 2-way associative.
Lastly, number of sets = 512 / (2 * 16) = 16

## Slide 29: Next time
How to properly choose cache parameters?
  Start by classifying why misses occur
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah