## Slide 1: EECS 370 - Lecture 22
Multi-Level Page Tables
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link

## Slide 2: Announcements
P4
  Last project!
  Due Thu (4/13)
HW 6
  Last homework!
  Due Monday (4/17)
Final exam
  …Last exam!
  Thu (4/20) @ 10:30 am
  Sample exams will be posted by early next week
  (One sample exam given in homework)

## Slide 3: Reminder
We use a “page table” to translate “virtual” addresses (specified by the programmer / assembler) to “physical” addresses (sent to memory)
  Allows multiple programs to run without interfering with each other
  Allows programs to use more storage than available in DRAM
    By mapping virtual addresses to disk instead of DRAM

## Slide 4: Class Problem (continued)
Virt addr | Virt page | Page fault? | Phys addr
0x00F0C | 0x0 | N | 0x1F0C
0x01F0C | 0x1 | N | 0x2F0C
0x20F0C | 0x20 | Y (into 3) | 0x3F0C
0x00100 | 0x0 | N | 0x1100
0x00200 | 0x0 | N | 0x1200
0x30000 | 0x30 | Y (into 2) | 0x2000
0x01FFF | 0x1 | Y (into 3) | 0x3FFF
0x00200 | 0x0 | N | 0x1200
4KB page size,
physical memory of 16KB, page table stored in physical page 0 and can never be evicted, 20 bit, byte-addressable virtual address space.
The page table initially has virtual page 0 in physical page 1, virtual page 1 in physical page 2 and no valid data in other physical pages.

## Slide 5: Size of the page table
How big is a page table entry?
  For 32-bit virtual address:
    If the machine can support 1GB = 230 bytes of physical memory and we use pages of size 4KB = 212,
    then the physical page number is 30-12 = 18 bits. Plus another valid bit + other useful stuff (read only, dirty, etc.)
    Let say about 3 bytes.
How many entries in the page table?
  1 entry per virtual page
  ARM virtual address is 32 bits – 12 bit page offset = 20
  Total number of virtual pages = 220
Total size of page table = Number of virtual pages
* Size of each page table entry
= 220 x 3 bytes ~ 3 MB

## Slide 6: How can you organize the page table?
Single-level page table occupies continuous region in physical memory
  Previous example always takes 3MB regardless of how much virtual memory is used
1
Physical page number
valid
…
A small program will use up 3MB to store just one PPN!!
It will be even worse for a 64-bit system!

## Slide 7: How can you organize the page table?
valid | PPN
1 | 0x1
1 | 0x2
1 | 0x3
valid | 2nd level page table
1 | 0x1000
valid | PPN
1 | 0x1
1 | 0x2
1 | 0x3
Option 2: Use a multi-level page table
  1st level page table (much smaller!) holds addresses 2nd level page tables
    2nd level page tables hold translation info, or 3rd level page tables if we wanna go deeper
    Only allocate space for 2nd level page tables that are used
Single-level: Tons of wasted space!
Common case: most programs use small portion of virtual memory space
Multi-level: Size is proportional to amount of memory used

## Slide 8: Hierarchical page table
Page table register
2nd level offset
Page offset
Page offset
1st level offset
Virtual
address
Physical page number
1st level page table
1
2nd level page table
valid
Physical
address
1
Physical page number
valid
2nd level page table
+
+
Fewer entries in 1st level page table than a single level page table
Only allocate space for the 2nd level page tables we actually need

## Slide 9: Hierarchical page table – 32bit Intel x86
How many bits in the virtual 1st level offset field?
How many bits in the virtual 2nd level offset field?
How many bits in the page offset?
How many entries in the 1st level page table?
2nd level offset
Page offset
1st level offset
Virtual
address
11
21
31
1st level offset
1st level page table
1
2nd level page table
valid
10
10
12
210=1024

## Slide 10: Hierarchical page table – 32bit Intel x86
How many bytes for each entry in the 1st level page table?
  4 bytes (address of 2nd level page)
Total size of 1st level page table
  4 bytes * 1024 entries = 4 KB
2nd level offset
Page offset
1st level offset
Virtual
address
11
21
31
1st level offset
1st level page table
1
2nd level page table
valid
1024 entries
Poll
4 bytes
Live Poll + Q&A: slido.com #eecs370

## Slide 11: Hierarchical page table
How many entries in the 2nd level of the page table?
  210 = 1024
How many bytes for each VPN in a 2nd level table?
  Let's round up to 4 bytes
Virtual
address
1st level page table
1
2nd level page table
valid
1
Physical page number
valid
2nd level page table
+
+
2nd level offset
Page offset
1st level offset
11
21
31

## Slide 12: Hierarchical page table – 32bit Intel x86
How many bits in the virtual 1st level offset field?
How many bits in the virtual 2nd level offset field?
How many bits in the page offset?
How many entries in the 1st level page table?
How many bytes for each entry in the 1st level page table?
How many entries in the 2nd level of the page table?
How many bytes for each entry in a 2nd level table?
What is the total size of the page table?
(here n is number of valid entries in the 1st level page table)
2nd level offset
Page offset
1st level offset
Virtual
address
11
21
31
Live Poll + Q&A: slido.com #eecs370

## Slide 13: Hierarchical page table – 32bit Intel x86
How many bits in the virtual 1st level offset field?
How many bits in the virtual 2nd level offset field?
How many bits in the page offset?
How many entries in the 1st level page table?
How many bytes for each entry in the 1st level page table?
How many entries in the 2nd level of the page table?
How many bytes for each entry in a 2nd level table?
What is the total size of the page table?
(here n is number of valid entries in the 1st level page table)
2nd level offset
Page offset
1st level offset
Virtual
address
11
21
31
10
10
12
210=1024
4
210=1024
~4
4K+n*4K

## Slide 14: Class Problem (32 bit x86)
What is the least amount of memory that could be used? When would this happen?
What is the most memory that could be used? When would this happen?
How much memory is used for this memory access pattern: 0x00000ABC 0x00000ABD 0x10000ABC 0x20000ABC
How much memory if we used a single-level page table with 4KB pages? Assume entries are rounded to the nearest word (4B)
Poll
Live Poll + Q&A: slido.com #eecs370

## Slide 15: Class Problem (32 bit x86)
What is the least amount of memory that could be used? When would this happen?
  4KB for 1st level page table. Occurs when no memory has been accessed (before program runs)
What is the most memory that could be used? When would this happen?
  4KB for 1st level page table + 1024*4KB for all possible 2nd level page tables = 4100KB (which slightly greater than 4096KB)
  Occurs when program uses all virtual pages (= 220 pages)

## Slide 16: Class Problem (32 bit x86)
How much memory is used for this memory access pattern:
0x00000ABC // Page fault 0x00000ABD 0x10000ABC // Page fault 0x20000ABC // Page fault
4KB for 1st level page table + 3*4KB for each 2L page table = 16 KB

## Slide 17: Class Problem (32 bit x86)
How much memory if we used a single-level page table with 4KB pages? Assume entries are rounded to the nearest word (4B)

## Slide 18: Class Problem (32 bit x86)
How much memory if we used a single-level page table with 4KB pages? Assume entries are rounded to the nearest word (4B)
  32 bits – 12 bit page offset = 20 bits of address
  2^20 (num entries) * 4B => 4MB

## Slide 19: Class Problem – Multi-level VM
Design a two-level virtual memory system of a byte addressable processor with 24-bit long addresses. No cache in the system. 256Kbytes of memory installed, and no additional memory can be added.
  Virtual memory page: 512 Bytes. Each page table entry must be an integer number of bytes, and must be the smallest size required to fit the physical page number + 1 bit to mark valid-entry
  We want each second-level page table to fit exactly in one memory page, and 1st level page table entries are 3 bytes each (a memory address pointer to a 2L page table).
Compute:
  Number of entries in each 2nd level page table;
  Number of virtual address bits used to index the 2nd level page table;
  Number of virtual address bits used to index the 1st level page table;
  Size of the 1st level page table.

## Slide 20: Class Problem – Multi-level VM

## Slide 21: Class Problem – Multi-level VM
Page Offset: 9 bits (512B page size)
Page offset = 9b
Physical page number = 9b
Physical address = 18b (256KB Mem size)
Physical page number = 18b (256KB mem size) – 9b (offset)
2nd level = 8b
Page offset = 9b
1st level = 7b
Virtual address = 24b
2nd level page table entry size: 9b (physical page number) + 1b =~ 2 bytes
2nd level page table fits exactly in 1 page
#entries in 2nd level page table is 512 bytes / 2 bytes = 256
#entries in 2nd level page table = 256 ➜Virtual page bits = 8b
Virtual 1st level page bits = 24 – 8 – 9 = 7b
1st level page table size = 2^7 * 3 bytes = 384B

## Slide 22: Page Replacement Strategies
Page table indirection enables a fully associative mapping between virtual and physical pages.
How do we implement LRU in OS?
  True LRU is expensive, but LRU is a heuristic anyway, so approximating LRU is fine
  Keep a “accessed” bit per page, cleared occasionally by the operating system. Then pick any “unaccessed” page to evict

## Slide 23: Other VM Translation Functions
Page data location
  Physical memory, disk, uninitialized data
Access permissions
  Read only pages for instructions
  This is how your system detects segmentation faults
Gathering access information
  Identifying dirty pages by tracking stores
  Identifying accesses to help determine LRU candidate

## Slide 24: Performance of Virtual Memory
To translate a virtual address into a physical address, we must first access the page table in physical memory
Then we access physical memory again to get the data
  A load instruction performs at least 2 memory reads
  A store instruction performs at least 1 read and then a write
Above lookup steps are SLOW

## Slide 25: Translation look-aside buffer (TLB)
We fix this performance problem by avoiding main memory in the translation from virtual to physical pages.
Buffer common translations in a Translation Look-aside Buffer (TLB), a fast cache memory dedicated to storing a small subset of valid V-to-P translations.
16-512 entries common.
Generally has low miss rate (< 1%).

## Slide 26: Translation look-aside buffer (TLB)
Virtual page
v
tag
Physical page
Pg offset
Virtual address
TLB

## Slide 27: Where is the TLB lookup?
We put the TLB lookup in the pipeline after the virtual address is calculated and before the memory reference is performed
  This may be before or during the data cache access.
    To be discussed next time
  In case of a TLB miss, we need to perform the virtual to physical address translation during the memory stage of the pipeline.

## Slide 28: Putting it all together
Loading your program in memory
  Ask operating system to create a new process
  Construct a page table for this process
  Mark all page table entries as invalid with a pointer to the disk image of the program
    That is, point to the executable file containing the binary.
  Run the program and get an immediate page fault on the first instruction.

## Slide 29
Loading a program into memory
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
References
0x0000
0x0004
0x7FFC
0x0008
0x2134
Physical Refs
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
Page size = 4 KB, Page table entry size = 4 B
Page table register points to physical address 0x0000

## Slide 30
Step 1: Read executable header & initialize page table
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
reserved
D1000
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 31
Step 2: Load PC from header & start execution
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
reserved
D1000
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
MISS!
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 32
Fetching instruction 0000
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
reserved
D1000
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 33
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
reserved
M1
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
M1
0
text1
ro
Fetching instruction 0000
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 34
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
reserved
M1
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
M1
0
text1
ro
Fetching instruction 0000
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 35
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
0x1004
reserved
M1
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
M1
0
text1
ro
HIT!
Fetching instruction 0004
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 36
Reference 7FFC
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
0x1004
reserved
M1
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
M1
0
text1
ro
MISS!
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 37
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
0x1004
0x0007
No map page fault
reserved
M1
D1001
D1002
no map
no map
no map
no map
no map
ro
ro
M1
0
text1
ro
Reference 7FFC
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 38
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
0x1004
0x0007
No map page fault
0x2FFC
reserved
M1
D1001
D1002
no map
no map
no map
no map
M2
ro
ro
M1
0
text1
ro
M2
7
rw
set to 0s
Reference 7FFC
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 39
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
0x1004
0x0007
No map page fault
0x2FFC
0x1008
reserved
M1
D1001
D1002
no map
no map
no map
no map
M2
ro
ro
M1
0
text1
ro
M2
7
rw
set to 0s
HIT!
Fetching instruction 0008
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 40
Reference 2134
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
References
0x0000
0x0004
0x7FFC
0x0008
0x2134
Physical Refs
0x0000
Page fault
0x1000
0x1004
0x0007
No map page fault
0x2FFC
0x1008
reserved
M1
D1001
D1002
no map
no map
no map
no map
M2
ro
ro
M1
0
text1
ro
M2
7
rw
set to 0s
MISS!
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003

## Slide 41
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
0x1004
0x0007
No map page fault
0x2FFC
0x1008
0x0002
Page fault
reserved
M1
D1001
D1002
no map
no map
no map
no map
M2
ro
ro
M1
0
text1
ro
M2
7
rw
set to 0s
Reference 2134
VPN PPN Permission
D0
D1
D2
D3
D1000
D1001
D1002
D1003
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 42
text2
global data
text1
Disk Pages
2 entry TLB
Memory
Page Table
D0
D1
D2
D3
D1000
D1001
D1002
D1003
0
1
2
3
4
5
6
7
Physical Refs
0x0000
Page fault
0x1000
0x1004
0x0007
No map page fault
0x2FFC
0x1008
0x0002
Page fault
0x3134
reserved
M1
D1001
M3
no map
no map
no map
no map
M2
ro
ro
M1
0
text1
ro
M3
2
rw
set to 0s
global data
Reference 2134
VPN PPN Permission
References
0x0000
0x0004
0x7FFC
0x0008
0x2134

## Slide 43: Next time
Speeding up virtual memory
  Adding caches
Wrap up class!
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah