## Slide 1: EECS 370 - Lecture 23
Final Review
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link

## Slide 2: Announcements
Final exam Thursday April 20th 10:30a - 12:30p
As with the midterm, you can have one 8.5 by 11 inch piece of paper with notes.
  If you need anything from the ARM/LEG ISA we will supply the LEG “green sheet”.
  We will assume you know (or have written on your page) LC2K instructions (though not LC2K encodings).
    So you should know what “lw 0 3 Bob” does.
Room assignments on Piazza by Tuesday evening.

## Slide 3: Important topics
Covers all course material with emphasis pipelining and afterwards.
  Pipelining, data, and control hazards
  Caches
  Virtual memory
  Performance
Material presented in lectures, homeworks, discussions, projects

## Slide 4: Exam Strategy
Pace yourself
Do not spend all your time on a single question
  If you don’t understand a question, move ahead & come back to it later
Answer as many questions as possible
  Give yourself a few minutes at the end to check your work and/or attempt to solve easy questions that you have not attacked yet

## Slide 5: Preparing for the exam
Review the lectures
Know how to solve the homework problems
Practice exams w/solutions are posted to course website
  Complete without looking at the solutions!

## Slide 6: Best way to review for the exam
Practice,
Practice,
Practice
Plenty of choices: Old Exams, Class Problems, Midterm Review Problems

## Slide 7: Selected Practice Questions
Just because it is not covered in this review it does not mean that it is not important
This review focuses on the newest material (because you’ve had less practice with it)
First question is warmup 

## Slide 8: Problem 1: Multiple Choice (first 12…)
In ARM, the first 4 parameters to a function are stored in registers and the remaining parameters are stored in the stack / heap / data / virtual​ section of memory.
Moore’s / Mealy’s / Dennard’s / Immerman’s​ Law states that the number of transistors on a single chip will double every 2 years.
All instructions in a CISC / RISC / multi-core​ architecture (usually) have the same length.

## Slide 9: Problem 1: Multiple Choice (first 12…)
The ​compiler / assembler / linker / loader​ is used to combine multiple object files into an executable program.
The ​compiler / assembler / linker / loader​ is used every time an executable program is run.

## Slide 10: Problem 1: Multiple Choice (first 12…)
The output of combinational / sequential​ circuits depends exclusively on the current input.
Functions that don’t call any functions (leaf functions) need not save and restore caller save / callee save / odd numbered​ registers.
If a cache includes dirty bits, then it must be using a write-back / write-through / allocate-on-write / not allocate-on-write​ policy.

## Slide 11: Problem 1: Multiple Choice (first 12…)
The single-cycle / multi-cycle / pipelined​ datapath has the lowest CPI among the three types of datapath discussed in class.
A 1-way set associative cache is the same as a fully associative / direct mapped / virtually addressed / physically addressed​ cache.
Direct-mapped caches reduce the cost of finding the correct data by minimizing the number of block offset / line index / tag / LRU comparisons.

## Slide 12: Problem 2 – Virtual Memory
Assume the following:
Virtual address size : 128 bytes; Page size : 16 bytes
Physical memory size : 8 pages; One-level page table of size : 16 bytes
Page replacement policy : LRU
Notes:
On a page fault, the page table is updated before allocating a physical page.
If more than one free page is available, the smallest physical page number is chosen.
Physical page #0 is reserved for the operating system (OS). It cannot be replaced.
If no mapping is found for a given virtual page assume the data is brought in from the disk.

## Slide 13: Problem 2 – Virtual Memory (cont.)
a. The initial state of physical memory is shown on the left. Complete the page table for Process ID 11 (PID: 11) on the right.
Physical Page # (PPN) | Memory Contents
0x0 | Reserved for OS
0x1 | Page Table of PID 11
0x2 | PID 11: VPN 0
0x3 | 
0x4 | PID 11: VPN 4
0x5 | PID 11: VPN 7
0x6 | 
0x7 | 
Virtual Page # (VPN) | Valid | Physical Page # (PPN)
0x0 |  | 
0x1 |  | 
0x2 |  | 
0x3 |  | 
0x4 |  | 
0x5 |  | 
0x6 |  | 
0x7 |  | 
Page Table of PID:11
Notes: Assume the following:
Virtual address size : 128 bytes; Page size : 16 bytes
Physical memory size : 8 pages; One-level page table of size : 16 bytes
Page replacement policy : LRU
Notes:
On a page fault, the page table is updated before allocating a physical page.
If more than one free page is available, the smallest physical page number is chosen.
Physical page #0 is reserved for the operating system (OS). It cannot be replaced.
If no mapping is found for a given virtual page assume the data is brought in from the disk

## Slide 14: Problem 2 – Virtual Memory (solution)
a. The initial state of physical memory is shown on the left. Complete the page table for Process ID 11 (PID: 11) on the right.
Physical Page # (PPN) | Memory Contents
0x0 | Reserved for OS
0x1 | Page Table of PID 11
0x2 | PID 11: VPN 0
0x3 | 
0x4 | PID 11: VPN 4
0x5 | PID 11: VPN 7
0x6 | 
0x7 | 
Virtual Page # (VPN) | Valid | Physical Page # (PPN)
0x0 | 1 | 0x2
0x1 | 0 | 
0x2 | 0 | 
0x3 | 0 | 
0x4 | 1 | 0x4
0x5 | 0 | 
0x6 | 0 | 
0x7 | 1 | 0x5
Page Table of PID:11
Notes: Assume the following:
Virtual address size : 128 bytes; Page size : 16 bytes
Physical memory size : 8 pages; One-level page table of size : 16 bytes
Page replacement policy : LRU
Notes:
On a page fault, the page table is updated before allocating a physical page.
If more than one free page is available, the smallest physical page number is chosen.
Physical page #0 is reserved for the operating system (OS). It cannot be replaced.
If no mapping is found for a given virtual page assume the data is brought in from the disk

## Slide 15: Problem 2 – Virtual Memory (cont.)
b. Complete the following table for the given sequence of virtual address requests. Assume that the initial physical memory and page table state is shown in part a, above. *Process 7 begins at Time 1. Process 11 begins before Time 0, and ends after Time 5.
Time | PID | Virt. Addr (VA) | Virtual Page # (VPN) | Physical Page # (PPN) | Page Fault? (Y/N) | Physical Address (PA)
0 | 11 | 0x0A |  |  |  | 
1* | 7 | 0x0A |  |  |  | 
2 | 7 | 0x0B |  |  |  | 
3 | 11 | 0x21 |  |  |  | 
4 | 7 | 0x74 |  |  |  | 
5* | 7 | 0x35 |  |  |  | 
6 | 7 | 0x20 |  |  |  | 
Physical Page # (PPN) | Memory Contents
0x0 | Reserved for OS
0x1 | Page Table of PID 11
0x2 | PID 11: VPN 0
0x3 | Page Table of PID 7
0x4 | PID 11: VPN 4
0x5 | PID 11: VPN 7
0x6 | 
0x7 | 
Notes: Assume the following:
Virtual address size : 128 bytes; Page size : 16 bytes
Physical memory size : 8 pages; One-level page table of size : 16 bytes
Page replacement policy : LRU
Notes:
On a page fault, the page table is updated before allocating a physical page.
If more than one free page is available, the smallest physical page number is chosen.
Physical page #0 is reserved for the operating system (OS). It cannot be replaced.
If no mapping is found for a given virtual page assume the data is brought in from the disk

## Slide 16: Problem 2 – Virtual Memory (cont.)
b. Complete the following table for the given sequence of virtual address requests. Assume that the initial physical memory and page table state is shown in part a, above. *Process 7 begins at Time 1. Process 11 begins before Time 0, and ends after Time 5.
Time | PID | Virt. Addr (VA) | Virtual Page # (VPN) | Physical Page # (PPN) | Page Fault? (Y/N) | Physical Address (PA)
0 | 11 | 0x0A | 0x0 | 0x2 | N | 0x2A
1* | 7 | 0x0A | 0x0 | 0x6 | Y | 0x6A
2 | 7 | 0x0B | 0x0 | 0x6 | N | 0x6B
3 | 11 | 0x21 | 0x2 | 0x7 | Y | 0x71
4 | 7 | 0x74 | 0x7 | 0x4 | Y | 0x44
5* | 7 | 0x35 | 0x3 | 0x5 | Y | 0x55
6 | 7 | 0x20 | 0x2 | 0x1 | Y | 0x10
Physical Page # (PPN) | Memory Contents
0x0 | Reserved for OS
0x1 | Page Table of PID 11
0x2 | PID 11: VPN 0
0x3 | Page Table of PID 7
0x4 | PID 11: VPN 4
0x5 | PID 11: VPN 7
0x6 | 
0x7 | 
Notes: Assume the following:
Virtual address size : 128 bytes; Page size : 16 bytes
Physical memory size : 8 pages; One-level page table of size : 16 bytes
Page replacement policy : LRU
Notes:
On a page fault, the page table is updated before allocating a physical page.
If more than one free page is available, the smallest physical page number is chosen.
Physical page #0 is reserved for the operating system (OS). It cannot be replaced.
If no mapping is found for a given virtual page assume the data is brought in from the disk

## Slide 17: Problem 3: Branch Prediction (F16)
Consider the following C code and corresponding LC2K assembly. Assume it is executed on a pipelined data-path with branch speculation discussed in class.
a) How many branch instructions are executed for a single run of the program?
int i, j, x = 0; for (i=0; i != 30; i++) { for (j=0; j != 2; j++) { x++; } } | lw 0 1 cnt1 lw 0 2 cnt2 lw 0 3 one outer noop beq 0 1 exit //B1 noop lw 0 2 cnt2 inner beq 0 2 done //B2 add 4 3 4 add 2 3 2 beq 0 0 inner //B3 done add 1 3 1 beq 0 0 outer //B4 exit halt cnt1 .fill 30 cnt2 .fill 2 one .fill -1
Notes: B1: 31 B2: 90 B3: 60 B4: 30

## Slide 18: Problem 3: Branch Prediction (F16)
Consider the following C code and corresponding LC2K assembly. Assume it is executed on a pipelined data-path with branch speculation discussed in class.
How many branch instructions are executed for a single run of the program?
B1: 31 B2: 90 B3: 60 B4: 30
int i, j, x = 0; for (i=0; i != 30; i++) { for (j=0; j != 2; j++) { x++; } } | lw 0 1 cnt1 lw 0 2 cnt2 lw 0 3 one outer noop beq 0 1 exit //B1 noop lw 0 2 cnt2 inner beq 0 2 done //B2 add 4 3 4 add 2 3 2 beq 0 0 inner //B3 done add 1 3 1 beq 0 0 outer //B4 exit halt cnt1 .fill 30 cnt2 .fill 2 one .fill -1
Notes: B1: 31 B2: 90 B3: 60 B4: 30

## Slide 19: Problem 3: Branch Prediction (F16)
Consider the following C code and corresponding LC2K assembly. Assume it is executed on a pipelined data-path with branch speculation discussed in class.
b) How many branches are predicted correctly if we predict Always-Not-Taken?
int i, j, x = 0; for (i=0; i != 30; i++) { for (j=0; j != 2; j++) { x++; } } | lw 0 1 cnt1 lw 0 2 cnt2 lw 0 3 one outer noop beq 0 1 exit //B1 noop lw 0 2 cnt2 inner beq 0 2 done //B2 add 4 3 4 add 2 3 2 beq 0 0 inner //B3 done add 1 3 1 beq 0 0 outer //B4 exit halt cnt1 .fill 30 cnt2 .fill 2 one .fill -1

## Slide 20: Problem 3: Branch Prediction (F16)
Consider the following C code and corresponding LC2K assembly. Assume it is executed on a pipelined data-path with branch speculation discussed in class.
b) How many branches are predicted correctly if we predict Always-Not-Taken? NT executions: B1: 30 B2: 60 B3: 0 B4: 0
int i, j, x = 0; for (i=0; i != 30; i++) { for (j=0; j != 2; j++) { x++; } } | lw 0 1 cnt1 lw 0 2 cnt2 lw 0 3 one outer noop beq 0 1 exit //B1 noop lw 0 2 cnt2 inner beq 0 2 done //B2 add 4 3 4 add 2 3 2 beq 0 0 inner //B3 done add 1 3 1 beq 0 0 outer //B4 exit halt cnt1 .fill 30 cnt2 .fill 2 one .fill -1
Total executions: B1: 31 B2: 90 B3: 60 B4: 30

## Slide 21: Problem 3: Branch Prediction (F16)
c) How many branches are predicted correctly if we use local last time 1-bit predictor?
Local 1-bit Predictor: In this prediction scheme, the PC of a branch instruction is used to index into a table. Each table entry for a branch is a 1-bit predictor, which predicts the same outcome as last time for that branch. Assume that the entries are initialized to Not Taken.
Local Last Time Predictor Table
int i, j, x = 0; for (i=0; i != 30; i++) { for (j=0; j != 2; j++) { x++; } } | lw 0 1 cnt1 lw 0 2 cnt2 lw 0 3 one outer noop beq 0 1 exit B1 noop lw 0 2 cnt2 inner beq 0 2 done B2 add 4 3 4 add 2 3 2 beq 0 0 inner B3 done add 1 3 1 beq 0 0 outer B4 exit halt cnt1 .fill 30 cnt2 .fill 2 one .fill -1
Branch PC
...
NT
T
NT
T
NT
T
NT
T
NT
T
NT
T
Notes: B1: 30 B2: 31 B3: 59 B4: 29
Total executions: B1: 31 B2: 90 B3: 60 B4: 30

## Slide 22: Problem 3: Branch Prediction (F16)
c) How many branches are predicted correctly if we use local last time 1-bit predictor?
Local 1-bit Predictor: In this prediction scheme, the PC of a branch instruction is used to index into a table. Each table entry for a branch is a 1-bit predictor, which predicts the same outcome as last time for that branch. Assume that the entries are initialized to Not Taken.
Local Last Time Predictor Table
B1: 30 B2: 31 B3: 59 B4: 29
Branch PC
...
NT
T
NT
T
NT
T
NT
T
NT
T
NT
T
int i, j, x = 0; for (i=0; i != 30; i++) { for (j=0; j != 2; j++) { x++; } } | lw 0 1 cnt1 lw 0 2 cnt2 lw 0 3 one outer noop beq 0 1 exit B1 noop lw 0 2 cnt2 inner beq 0 2 done B2 add 4 3 4 add 2 3 2 beq 0 0 inner B3 done add 1 3 1 beq 0 0 outer B4 exit halt cnt1 .fill 30 cnt2 .fill 2 one .fill -1

## Slide 23: Problem 4: Multi-level Page Tables
You need to design a 3-level hierarchical page table. Physical memory is with 8KB (byte-addressable); virtual memory addresses are 17-bits long. A page is 32 bytes & each page table entry is 2bytes. The 1st level table & each of the 2nd level & 3rd level page tables require precisely one page of storage.
a. Determine the bit positions for the following fields in a virtual address and a physical address.
Virtual Address |  |  | 
1st level offset | 2nd level offset | 3rd level offset | Page offset
Bits: | Bits: | Bits: | Bits:
Physical Address | 
Physical Page Number | Page offset
Bits: | Bits:
Notes: Bits:16-13
Bits:12-9
Bits:8-5
Bits:4-0
Bits:12-5
Bits:4-0

## Slide 24: Problem 4: Multi-level Page Tables (sol.)
You need to design a 3-level hierarchical page table. Physical memory is with 8KB (byte-addressable); virtual memory addresses are 17-bits long. A page is 32 bytes & each page table entry is 2bytes. The 1st level table & each of the 2nd level & 3rd level page tables require precisely one page of storage.
a. Determine the bit positions for the following fields in a virtual address and a physical address. Page offset field has been completed as an example.
Virtual Address |  |  | 
1st level offset | 2nd level offset | 3rd level offset | Page offset
Bits:16-13 | Bits:12-9 | Bits:8-5 | Bits:4-0
Physical Address | 
Physical Page Number | Page offset
Bits:12-5 | Bits:4-0

## Slide 25: Problem 4: Multi-level Page Tables
b. Assume that at the beginning of a program’s execution only the 1st level table is in main memory. For the program shown below, calculate the total size of all page tables (including the 1st level, 2nd level and 3rd level page tables) in main memory after executing the for loop. Assume the array BigArray is allocated at the virtual address 0x0 and ‘char’ = 1 byte. Show your work.
char BigArray[2048*32];
for (i = 0; i < 2048; i += 16){
sum += BigArray[i*32];
}
Total 2nd Level Page Tables?
Total 3rd Level Page Tables?
Total Size in memory?

## Slide 26: Problem 4: Multi-level Page Tables
b.
char BigArray[2048*32];
for (i = 0; i < 2048; i += 16){
sum += BigArray[i*32];
}
Notes: Total 2nd Level Page Tables? 8
Total 3rd Level Page Tables? 128
Total Size in memory? (1+8+128)*32Bytes = 4384Bytes

## Slide 27: Problem 4: Multi-level Page Tables (sol.)
b.
char BigArray[2048*32];
for (i = 0; i < 2048; i += 16){
sum += BigArray[i*32];
}
Total 2nd Level Page Tables? 8
Total 3rd Level Page Tables? 128
Total Size in memory? (1+8+128)*32Bytes = 4384Bytes

## Slide 28: Now you are a Computer Architect (yay!)
One architecture, many microarchitectures
If you like this stuff, take EECS 470, 482
Study for the final & have a fun summer!
"Leading a student to learning's treasures Gives a teacher untold pleasures!"

## Slide 30: What's next for You?!
What classes should you look at if your interested in this kind of stuff?

## Slide 31: More Classes?
EECS 470 – Computer Architecture
Picks up where we leave off in 370
Discuss more sophisticated enhancements to processor design
  Out-of-order execution
  Multi-core / multi-threaded processors
Major Design Experience / Capstone
  Work in teams to design an actual processor (not simulator) over the course of the semester
  LOT'S of work
Requires EECS 270
  For Verilog (a Hardware Description Language)

## Slide 32: More Classes?
EECS 373 – Embedded Systems
  Learn about parts of computer systems that aren't in the processor or cache
    Input/output
    Timers
    Bus interfaces
  Followed up by 473 (MDE / Capstone)
EECS 471 – Applied Parallel Programming with GPUs
  How are graphics processing units different than normal processors?
  How do we take advantage of their raw power when writing software?

## Slide 33: More Classes?
EECS 427 – VLSI Design
  Design a processor at the circuit level
  Actually layout all the transistors
  Less architecture – more circuit design
EECS 570 (Parallel Computer Architecture) + 573 (Microarchitecture)
  Learn about more current research into architecture
  Requires 470

## Slide 34: More Classes?
EECS 483 (Front-end compilers) + 583 (Back-end compilers)
  583 is more relevant to architecture
  How to design compilers to write efficient assembly?
  Requires knowledge of hardware optimizations
EECS 482 – Operating Systems
  How do moderns systems support multiple threads running simultaneously?
  How does OS manage virtual memory?
  How do file systems work?
EECS 388 – Computer Security
  How do things like caches "leak" information about a program's data?
  How can call stacks be tricked into executing arbitrary code?

## Slide 35: More Classes?
EECS 498-001 – Quantum Computing for the Computer Scientist
  Winter 23
  How can we redesign the computing stack to take advantage of the bizarre rules of quantum mechanics?
  Rather than having bits be 0 or 1, have quantum bits be in superpositions of 0 and 1
    Perform massive number of computations simultaneously… sort of
  Requires 370 and 281

## Slide 36: Other questions?!