## Slide 1: EECS 370 - Lecture 3
LC2K
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link

## Slide 3: Important Data
Chart: Does Your Neighbor Like Pineapple on Pizza?
| good | bad | neutral
 | 21 | 18 | 16

## Slide 4: Lingering Questions
"How does the compiler know what is what? For example how does the computer know that 100011 is supposed to be a char 'C' instead of an unsigned int of 67, or a signed int of -61."
  The compiler knows because the user will label a variable as "char" or "int" or "unsigned int"
  The hardware doesn't know or care: it's just 100011 and trusts that the program will execute the appropriate instructions
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah

## Slide 5: Announcements
HW 1
  Posted on website, due next Friday
P1
  3 parts, first part due in two weeks
Setup clinic
  Need help getting your debugger setup?
  Dedicated help on Friday!
  Homework 1 has a question requiring you to show debugger is setup
OH
  Going on now: see website->Google Calendar->Office Hours

## Slide 6: Instruction Set Architecture (ISA) Design Lectures
“People who are really serious about software should make their own hardware.” — Alan Kay
Lecture 2: ISA - storage types, binary and addressing modes
Lecture 3 : LC2K
Lecture 4 : ARM
Lecture 5 : Converting C to assembly – basic blocks
Lecture 6 : Converting C to assembly – functions
Lecture 7 : Translation software; libraries, memory layout
Notes: Known for
Dynabook object-oriented programming Smalltalk

## Slide 7: Reminder- System Organization
Memory
Registers
+
32 x 64 bits
CPU
Gigabytes to Terabytes
Load
Store
ALU
Address FFFF…
Address 0000
X0 | 0
X1 | 7
X2 | -3
0102
Program counter
0102
ADD X0, X1, X2
Address 0102
ADD X0, X1, X2
SUB X1, X2, X0
Let's execute this short program:

## Slide 8: Reminder- System Organization
Memory
Registers
+
32 x 64 bits
CPU
Gigabytes to Terabytes
Load
Store
ALU
Address FFFF…
Address 0000
X0 | 4
X1 | 7
X2 | -3
0103
Program counter
0103
SUB X1, X2, X0
Address 0103
ADD X0, X1, X2
SUB X1, X2, X0
Let's execute this short program:

## Slide 9: Reminder- System Organization
Memory
Registers
+
32 x 64 bits
CPU
Gigabytes to Terabytes
Load
Store
ALU
Address FFFF…
Address 0000
X0 | 4
X1 | -7
X2 | -3
0104
Program counter
ADD X0, X1, X2
SUB X1, X2, X0
Let's execute this short program:

## Slide 10: Encoding Instructions
We saw last time that binary numbers can represent signed and unsigned numbers, chars, and fractional numbers
But they must also represent instructions themselves!
  After all, memory is just a collection of 1s and 0s
We need a way of encoding instructions in order to store them in memory

## Slide 11: Software program to machine code
Example ISA
(simplified)

## Slide 12: Assembly Instruction Encoding
Since the EDSAC (1949) almost all computers stored program instructions the same way they store data.
Each instruction is encoded as a number
This is the number stored in memory!
011011010011001 = 20 + 23 + 24 + 27 + 29 + 210 + 212 + 213
= 13977
Poll: How many different "operation codes" could be supported by this ISA? How many registers?
Example ISA
(simplified)
Live Poll + Q&A: slido.com #eecs370

## Slide 13: What if we run out of registers?
Modern architectures give us between 4 and 64 registers
What if I want to sort a list of 1000 integers?
Need to make use of memory
Large array of storage accessed using memory addresses
  A machine with a 32 bit address can reference memory locations 0 to 232-1 (or 4,294,967,295).
  A machine with a 64 bit address can reference memory locations 0 to 264-1
  (or 18,446,744,073,709,551,615—18 exa-locations)
load instructions ready from memory, places in a register
store instructions write from register into memory
"We will never make a 32-bit operating system" - Bill Gates, 1983

## Slide 14: Memory architecture: The ARM (Linux) Memory Image
Machine code instructions (and some constants)
Reserved for operating system
Global data and static local data
Dynamically allocated data—new or malloc()
Stack frames: local variables, parameters, etc.
Stack
Heap data
Static data
Text
Reserved
0

## Slide 15: Addressing Modes
Direct addressing
Register indirect
Base + displacement
PC-relative

## Slide 16: Direct Addressing
Consider this code:
const double PI = 3.14;
double two_pi() {
return 2*PI;
}
When we load PI, it's ALWAYS the same address
  If the ISA supports it, we can just hardcode that address in the instruction
Like register addressing
  Specify address as immediate constant
  load r1, mem[1500] ; r1  contents of location 1500
  jump mem[3000] ; jump to address 3000
Useful for addressing locations that don’t change during execution
  Branch target addresses
  Global/static variable locations
Example ISA
(simplified)
Not practical in modern ISAs… if we have 32 bit instructions and 32 bit addresses, the entire instruction is the address!

## Slide 17: Register indirect
Consider this code:
int my_arr[2] = {6666, 7777};
int* ptr = &my_arr[0];
for(int i=0; i<2; i++) {
int x = *ptr;
ptr++;
}
Everytime we load into x, it's a different address
But the address is always stored in another variable
If ISA supports it, we could use a load like this
  load r1, mem[r2]
Example ISA
(simplified)

## Slide 18: Register indirect
Consider this code:
int my_arr[2] = {6666, 7777};
int* ptr = &my_arr[0];
for(int i=0; i<2; i++) {
int x = *ptr;
ptr++;
}
load r1, mem[ r2 ]
add r2, r2, #4
load r1, mem[ r2 ]
3340
7777
6666
3340
3344
R2
register file
memory
6666
R1
Example ISA
(simplified)

## Slide 19: Register indirect
Consider this code:
int my_arr[2] = {6666, 7777};
int* ptr = &my_arr[0];
for(int i=0; i<2; i++) {
int x = *ptr;
ptr++;
}
load r1, mem[ r2 ]
add r2, r2, #4
load r1, mem[ r2 ]
3344
7777
6666
3340
3344
R2
register file
memory
6666
R1
Example ISA
(simplified)

## Slide 20: Register indirect
Consider this code:
int my_arr[2] = {6666, 7777};
int* ptr = &my_arr[0];
for(int i=0; i<2; i++) {
int x = *ptr;
ptr++;
}
load r1, mem[ r2 ]
add r2, r2, #4
load r1, mem[ r2 ]
3344
7777
6666
3340
3344
R2
register file
memory
6666
R1
This is better, but we can be more general
Example ISA
(simplified)

## Slide 21: Base + Displacement
Consider this code:
struct My_Struct {
int tot;
//...
int val;
};
My_Struct a;
//...
a.tot += a.val;
If a register holds the starting address of "a"…
  Then the specific values needed are a slight offset
Base + Displacement
  reg value + immed
load r1, mem[r2 + 32]
2340
6666
5555
2340
2372
R2
register file
memory
Very general, most common addressing mode today

## Slide 22: Class Problem
10
100
108
100
108
R2
104
-1
0
R1
108
R3
r2 = load mem[r3]
r3 = load mem[r2+4]
store mem[r2+8], r3
a. What are the contents of register/memory after executing the following instructions
register file
memory
Poll: What are the contents of register / memory?
Notes: load Rx M[M[y] becomes
load Rt M[R0+ y]
load Rx M[Rt +0]

## Slide 23: PC-relative addressing
Relevant for P1.a!
Variant on base + displacement
Remember PC is "Program Counter", keeps track of which line (memory address) of the program we're at
PC register is base, longer displacement possible since PC is assumed implicitly (more bits available)
  Used for branch instructions
    jump [ - 8 ] ; jump back 2 instructions (32-bit instructions)

## Slide 24: ISA Types
Reduced Instruction Set Computing (RISC)
  Fewer, simpler instructions
  Encoding of instructions are usually the same size
  Simpler hardware
  Program is larger, more tedious to write by hand
  E.g. LC2K, RISC-V, ARM (kinda)
  More popular now
Complex Instruction Set Computing (CISC)
  More, complex instructions
  Encoding of instructions are different sizes
  More complex hardware
  Short, expressive programs, easier to write by hand
  E.g. x86
  Less popular now

## Slide 25: LC2K ISA
Notes: Why do we study LC2K? Its simplified to make the projects tractable. But, it’s a terrible ISA…

## Slide 26: Programming Assignment #1
  Write an assembler to convert input (assembly language program) to output (machine code version of program)
  “1a”
Write a behavioral simulator to run the machine code version of the program (printing the contents of the registers and memory after each instruction executes
  “1s”
Write an efficient LC2K assembly language program to multiply two numbers
  “1m”

## Slide 27: Programming Assignment #1
Where to start…
  Write some test cases to check your code
    Program 1: halt
    Program 2: noop
    halt
    Program 3: add 1 1 1
    halt
    Program 4: nor 1 1 1
    halt

## Slide 28: LC2K Processor
32-bit processor
  Instructions are 32 bits
  Integer registers are 32 bits
8 registers
  register 0 always gives the value 0
supports 65536 words of memory (addressable space)
8 instructions in the following common categories:
  Arithmetic: add
  Logical: nor
  Data transfer: lw, sw
  Conditional branch: beq
  Unconditional branch (jump) and link: jalr
  Other: halt, noop
LC2K ISA

## Slide 29: Instruction Encoding
Instruction set architecture defines the mapping of assembly instructions to machine code
add 1 2 3 // r3 = r1 + r2
regA
regB
unused
opcode
unused
destR
31-25
24-22
21-19
18-16
15-3
2-0
LC2K ISA

## Slide 30: Instruction Formats
Tells you which bit positions mean what
R (register) type instructions (add ‘000’, nor ‘001’)
I (immediate) type instructions (lw ‘010’, sw ‘011’, beq ‘100’)
regA
regB
unused
opcode
unused
destR
31-25
24-22
21-19
18-16
15-3
2-0
regA
regB
offset
opcode
unused
31-25
24-22
21-19
18-16
15-0
LC2K ISA

## Slide 31: Instruction Formats
J-type instructions (jalr ‘101’)
O type instructions (halt ‘110’, noop ‘111’)
regA
regB
opcode
unused
31-25
24-22
21-19
18-16
unused
opcode
unused
31-25
24-22
21-0
unused
15-0
LC2K ISA

## Slide 32: Bit Encodings
Opcode encodings
  add (000), nor (001), lw (010), sw (011), beq (100), jalr (101), halt (110), noop (111)
Register values
  Just encode the register number (r2 = 010)
Immediate values
  Just encode the values in 2’s complement format
LC2K ISA

## Slide 33: Example Encoding - nor
nor 3 4 7 (r7 = r3 nor r4)
regA
regB
unused
opcode
unused
destR
31-25
24-22
21-19
18-16
15-3
2-0
0000000
001
011
100
0000000000000
111
Convert to Hex  0x005C0007
Convert to Dec  6029319
LC2K ISA

## Slide 34: Example Encoding - lw
lw 5 2 -8 (r2 = mem[r5 + -8])
regA
regB
offset
opcode
unused
31-25
24-22
21-19
18-16
15-0
0000000
010
101
010
1111111111111000
Convert to Hex  0x00AAFFF8
Convert to Dec  11206648
LC2K ISA
Note that we "bit-extend" 1 for negative numbers

## Slide 35: Another way to think about the assembler
Each line of assembly code corresponds to a number
  “add 0 0 0” is just 0.
  “lw 5 2 -8” is 11206648
We only write in assembly because it’s easier to read.

## Slide 36: .fill
I also might want a number, to be, well, a number.
  Maybe I want the number 7 as a data element I can use.
.fill tells the assembler to put a number instead of an instruction
The syntax is just “.fill 7”.
Question:
  What do “.fill 7” and “add 0 0 7” have in common?

## Slide 37: .fill
.fill is NOT an instruction
It does not have a corresponding opcode
It should be used to initialize data in your program
  If your PC ever points to it, something wrong has probably happened
But if the PC DOES point to it, it will treat it as whatever type of instruction encodes to that number
IMPORTANT!

## Slide 38: Labels in LC2K
Labels are used in lw/sw instructions or beq instruction
For lw or sw instructions, the assembler should compute offsetField to be equal to the address of the label
  i.e. offsetField = address of the label
For beq instructions, the assembler should translate the label into the numeric offsetField needed to branch to that label
  i.e. PC+1+ offsetField = address of the label
Notes: Loop=0; tom=2, end=4

## Slide 39: Labels in LC2K
Labels are a way of referring to a line number in an assembly program.
  loop beq 3 4 end
  noop
  beq 0 0 loop
  end halt
Here loop is 0 and end is 3.
What are the values of the labels here?
  loop beq 3 4 end
  add 3 3 3
  tom noop
  beq 0 0 loop
  end halt
Poll: What are the labels replaced with?
// this is the assembly for:
while(x != y) {
x *= 2;
}
Notes: Loop=0; tom=2, end=4

## Slide 40: Next Time
The ARM ISA
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah
Live Poll + Q&A: slido.com #eecs370

## Slide 41: Extra Problem 1
Compute the encoding in Hex for:
  add 3 7 3 (r3 = r3 + r7) (add = 000)
  sw 1 5 67 (M[r1+67] = r5) (sw = 011)
regA
regB
offset
opcode
unused
31-25
24-22
21-19
18-16
15-0
regA
regB
unused
opcode
unused
destR
31-25
24-22
21-19
18-16
15-3
2-0
LC2K ISA
0000000 000 011 111 000…000 011
0000000 011 001 101 0000000001000011
Notes: 0x001F 0003
0x00CD 0043

## Slide 42: Extra problem 2
  loop lw 0 1 one
  add 1 1 1
  sw 0 1 one
  halt
  one .fill 1
What does that program do?
Be aware that a beq uses PC-relative addressing.
  Be sure to carefully read the example in project 1.
Poll: What's the first line in binary?
Notes: lw=010; 0=000; 1=001; one=0000000000000100
0000000 010 000 001 0000000000000100
0000 0000 1000 0001 0000 0000 0000 0100