## Slide 1: EECS 370 - Lecture 6
Function Calls
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link
Poll: Who is responsible for erasing a whiteboard in a public space?
The person who is done using it
The person who is about to use it

## Slide 2: Announcements
P1
  Part a due Thu @ 11:59 via Autograder
  Project 1 s + m due Thu 1/26
HW 2
  Posted on website, due Mon 2/6 at 8 pm
Get exam conflicts and SSD accommodations sent to us ASAP
  Forms listed on the website

## Slide 3: Instruction Set Architecture (ISA) Design Lectures
Lecture 2: ISA - storage types, binary and addressing modes
Lecture 3 : LC2K
Lecture 4 : ARM
Lecture 5 : Converting C to assembly – basic blocks
Lecture 6 : Converting C to assembly – functions
Lecture 7 : Translation software; libraries, memory layout
Notes: Known for
Dynabook object-oriented programming Smalltalk

## Slide 4: ARM/LEGv8 Sequencing Instructions
Sequencing instructions change the flow of instructions that are executed
  This is achieved by modifying the program counter (PC)
Unconditional branches are the most straightforward they ALWAYS change the PC and thus “jump” to another instruction out of the usual sequence
Conditional branches
If (condition_test) goto target_address
  condition_test examines the four flags from the processor status word (SPSR)
  target_address is a 19 bit signed word displacement on current PC

## Slide 5: LEGv8 Conditional Instructions
Two varieties of conditional branches
  One type compares a register to see if it is equal to zero.
  Another type checks the condition codes set in the status register.
Talked about CBZ and CBNZ last time
Let's look at B.cond now

## Slide 6: LEGv8 Conditional Instructions
Motivation:
  Some types of branches makes sense to check if a certain value is zero or not
    while(a)
  But not all:
    if(a > b)
    if(a == b)
  Using an extra program status register to check for various conditions allows for a greater breadth of branching behavior

## Slide 7: LEGv8 Conditional Instructions Using FLAGS
FLAGS: NZVC record the results of (arithmetic) operations Negative, Zero, oVerflow, Carry—not present in LC2K
We explicitly set them using the “set” modification to ADD/SUB etc.
Example: ADDS causes the 4 flag bits to be set according as the outcome is negative, zero, overflows, or generates a carry

## Slide 8: ARM Condition Codes Determine Direction of Branch
In LEGv8 only ADDS / SUBS / ADDIS / SUBIS / CMP /CMPI set the condition codes FLAGs or condition codes in PSR—the program status register
Four primary condition codes evaluated:
  N – set if the result is negative (i.e., bit 63 is non-zero)
  Z – set if the result is zero (i.e., all 64 bits are zero)
  C – set if last addition/subtraction had a carry/borrow out of bit 63
  V – set if the last addition/subtraction produced an overflow (e.g., two negative numbers added together produce a positive result)
Don’t worry about the C and V for this class

## Slide 9: ARM Condition Codes Determine Direction of Branch--continued
Need to know the 7 with the red arrows

## Slide 10: Conditional Branches: How to use
CMP instruction lets you compare two registers.
  Could also use SUBS etc.
    That could save you an instruction.
B.cond lets you branch based on that comparison.
Example:
  Branches to Label1 if X1 is greater than X2.
CMP X1, X2
B.GT Label1

## Slide 11: Branch—Example
Convert the following C code into LEGv8 assembly (assume x is in X1, y in X2):
int x, y;
if (x == y)
x++;
else
y++;
// …
Live Poll + Q&A: slido.com #eecs370

## Slide 12: Branch—Example
Convert the following C code into LEGv8 assembly (assume x is in X1, y in X2):
int x, y;
if (x == y)
x++;
else
y++;
// …
CMP X1, X2
B.NE 3 ADD X1, X1, #1
B 2
ADD X2, X2, #1
CMP X1, X2
B.NE L1 ADD X1, X1, #1
B L2
L1: ADD X2, X2, #1
L2: …
Without Labels
Using Labels
Assemblers must deal with labels and assign displacements
Note that conditions in assembly are often the inverse of the "if" condition. Why?

## Slide 13: Loop—Example
// assume all variables are long long integers (64 bits or 8 bytes)
// i is in X1, start of a is at address 100, sum is in X2
sum = 0;
for (i=0 ; i < 10 ; i++) {
if (a[i] >= 0) {
sum += a[i];
}
}
MOV X1, XZR
MOV X2, XZR
Loop1: CMPI X1, #10
B.EQ endLoop
LSL X6, X1, #3 LDUR X5, [X6, #100]
CMPI X5, #0
B.LT endif
ADD X2, X2, X5
endif: ADDI X1, X1, #1
B Loop1
endLoop:
# of branch instructions
= 3*10 + 1= 31
a.k.a. while-do template
Notes: MOVs are wrong…... ANDI X1, X1, #0 etc
(Z=0 & N=V)
  Use of MOV pseudo instruction ORR X12, XZR, X12 moves X12 to X2
it's called loop induction ($1 increments by 4)
what if the address was not 500 but was instead 3ffffff ?
you would load $1 with the proper initial address instead of 0
(real induction does that)

## Slide 14: Extra Example: Do-while Loop
// assume all variables are long long integers (64 bits or 8 bytes)
// i is in X1, start of a is at address 100, sum is in X2
sum = 0;
for (i=0 ; i < 10 ; i++) {
if (a[i] >= 0) {
sum += a[i];
}
}
MOV X1, XZR
MOV X2, XZR
Loop1: LSL X6, X1, #3 LDUR X5, [X6, #100]
CMPI X5, #0
B.LT endif
ADD X2, X2, X5
endIf: ADDI X1, X1, #1
CMPI X1, #10
B.LT Loop1
endLoop:
# of branch instructions
= 2*10 = 20
a.k.a. do-while template
Look through this on your own
Notes: Given these are constants, we dropped the “outside of the loop” top test (it’s going to happen once). Should it be readded?
Instead of using MOV X4 #10, could have used a CMPI to 10. That would probably be better?

## Slide 15: Extra Problem – For Your Reference
Write the ARM assembly code to implement the following C code:
// assume ptr is in X1
// struct {int val; struct node *next;} node;
// struct node *ptr;
if ((ptr != NULL) && (ptr->val > 0))
ptr->val++;

## Slide 16: Extra Problem
Write the ARM assembly code to implement the following C code:
cmp r1, #0
beq Endif
ldursw r2, [r1, #0]
cmp r2, #0
b.le Endif
add r2, r2, #1
str r2, [r1, #0]
Endif : ….
// assume ptr is in X1
// struct {int val; struct node *next;} node;
// struct node *ptr;
if ((ptr != NULL) && (ptr->val > 0))
ptr->val++;

## Slide 17: Branching far away
Underlying philosophy of ISA design: make the common case fast
Most branches target nearby instructions
  Displacement of 19 bits is usually enough
BUT what if we need to branch really far away (more than 219 words)?
  CBZ X15, FarLabel
The assembler is smart enough to replace that with
  CBNZ X15, L1
  B FarLabel
  L1: ……..
The simple branch instruction (B) has a 26 bit offset which spans about 64 million instructions!
In LC2K, we can do a similar thing by using JALR instead of BEQ

## Slide 18: Unconditional Branching Instructions
There are three types of unconditional branches in the LEGv8 ISA.
  The first (B) is the PC relative branch with the 26 bit offset from the last slide.
  The second (BR) jumps to the address contained in a register (X30 above)
  The third (BL) is like our PC relative branch but it does something else.
    It sets X30 (always) to be the current PC+4 before it branches.
Why is BL storing PC+4 into a register?

## Slide 19: Branch with Link (BL)
Branch with Link is the branch instruction used to call functions
  Functions need to know where they were called from so they can return.
    In particular they will need to return to right after the function call
    Can use “BR X30”
Say that we execute the instruction BL #200 when at PC 1000.
  What address will be branched to?
  What value is stored in X30?
  How is that value in X30 useful?
Poll
Live Poll + Q&A: slido.com #eecs370

## Slide 20: Converting function calls to assembly code
C: factorial(5);
  Need to pass parameters to the called function—factorial
  Need to save return address of caller so we can get back
  Need to save register values (why?)
  Need to jump to factorial
  Need to get return value (if used)
  Restore register values
Execute instructions for factorial()
Jump to return address

## Slide 21: Task 1: Passing parameters
Where should you put all of the parameters?
  Registers?
    Fast access but few in number and wrong size for some objects
  Memory?
    Good general solution but slow
ARMv8 solution—and the usual answer:
  Both
    Put the first few parameters in registers (if they fit) (X0 – X7)
    Put the rest in memory on the call stack— important concept

## Slide 22: Call stack
ARM conventions (and most other processors) allocate a region of memory for the “call” stack
  This memory is used to manage all the storage requirements to simulate function call semantics
    Parameters (that were not passed through registers)
    Local variables
    Temporary storage (when you run out of registers and need somewhere to save a value)
    Return address
    Etc.
Sections of memory on the call stack [stack frames] are allocated when you make a function call, and de-allocated when you return from a function

## Slide 23: The stack grows as functions are called
void foo()
{
int x, y[2];
bar(x);
}
void bar(int x)
{
int a[3];
printf();
}
foo’s stack frame
inside foo
foo calls bar
foo’s stack frame
bar’s stack frame
bar calls printf
foo’s stack frame
bar’s stack frame
printf’s stack frame
FUNCTION CALLS

## Slide 24: The stack shrinks as functions return
foo’s stack frame
bar returns
printf returns
foo’s stack frame
bar’s stack frame
FUNCTION CALLS
void foo()
{
int x, y[2];
bar(x);
}
void bar(int x)
{
int a[3];
printf();
}

## Slide 25: Stack frame contents
x
return addr to main
y[0]
spilled registers in foo
y[1]
foo’s stack frame
FUNCTION CALLS
void foo()
{
int x, y[2];
bar(x);
}
void bar(int x)
{
int a[3];
printf();
}
Notes: Spilled means put in memory rather than registers.
A "spilled variable" is a variable in main memory rather than in a CPU register. The operation of moving a variable from a register to memory is called spilling, while the reverse operation of moving a variable from memory to a register is called filling. For example, a 32-bit variable spilled to memory gets 32 bits of stack space allocated and all references to the variable are then to that memory. Such a variable has a much slower processing speed than a variable in a register. When deciding which variables to spill, multiple factors are considered: execution time, code space, data space.

## Slide 26: Stack frame contents (2)
x
return addr to foo
a[0]
a[1]
a[2]
spilled regs in bar
foo’s frame
bar’s frame
x
return addr to main
y[0]
spilled regs in foo
y[1]
foo calls bar
FUNCTION CALLS
Spill data-–not enough room in x0-x7 for params and also caller and callee saves
void foo()
{
int x, y[2];
bar(x);
}
void bar(int x)
{
int a[3];
printf();
}

## Slide 27: Assigning variables to memory spaces
int w;
void foo(int x)
{
static int y[4];
char* p;
p = malloc(10);
//…
printf(“%s\n”, p);
}
static
text
stack
heap
FUNCTION CALLS
Review: Where do the variables go?
Live Poll + Q&A: slido.com #eecs370
Notes: 27

## Slide 28: Assigning variables to memory spaces
int w;
void foo(int x)
{
static int y[4];
char* p;
p = malloc(10);
//…
printf(“%s\n”, p);
}
static
text
stack
heap
w goes in static, as it’s a global
x goes on the stack, as it’s a parameter
y goes in static, 1 copy of this!!
p goes on the stack
allocate 10 bytes on heap, ptr
set to the address
string goes in static, pointer
to string on stack, p goes on
stack
FUNCTION CALLS
TODO: add slides on how to access local variables via SP
The addresses of local variables will be different depending on where we are in the call stack
ld r13, r1, STACK
// Here, r13 is holding the offset of how far we are down the stack
Notes: 28

## Slide 29: What about registers?
Higher level languages (like C/C++) provide many abstractions that don't exist at the assembly level
E.g. in C, each function has its own local variables
  Even if different function have local variables with the same name, they are independent and guaranteed not to interfere with each other!
void foo(){
int a=1;
bar();
printf(a);
}
void bar(){
int a=2;
return;
}
Still prints "1"… these don't interfere

## Slide 30: What about registers?
But in assembly, all functions share a small set (e.g. 32) of registers
  Called functions will overwrite registers needed by calling functions
"Someone" needs to save/restore values when a function is called to ensure this doesn't happen
main: movz X0, #1
bl foo
bl printf
foo: movz X0, #2
br X30
foo() overwrites X0 if we don't do something!!

## Slide 31: Two Possible Solutions
Either the called function saves register values before it overwrites them and restores them before the function returns (callee saved)…
Or the calling function saves register values before the function call and restores them after the function call (caller saved)…
main: movz X0, #1
bl foo
bl printf
foo: stur X0, [stack]
movz X0, #2
ldur X0, [stack]
br X30
main: movz X0, #1
stur X0, [stack]
bl foo
ldur X0, [stack]
bl printf
foo: movz X0, #2
br X30

## Slide 32: Another example
void foo(){
int a,b,c,d;
a = 5; b = 6;
c = a+1; d=c-1;
bar();
d = a+d;
return();
}
void foo(){
int a,b,c,d;
a = 5; b = 6;
c = a+1; d=c-1;
save r1 to stack save r4 to stack
bar();
restore r1
restore r4
d = a+d;
return();
}
void foo(){
int a,b,c,d;
save r1
save r2
save r3
save r4
a = 5; b = 6;
c = a+1; d=c-1;
bar();
d = a+d;
restore r1
restore r2
restore r3
restore r4
return();
}
Original C Code
Additions for Caller-save
Additions for Callee-save
Assume bar() will overwrite registers holding a,d
bar() will save a,b, but now foo() must save main's variables
a->r1, b->r2, etc.
No need to save r2/r3. Why?

## Slide 33: “caller-save” vs. “callee-save”
Caller-save
  What if bar() doesn't use r1/r4?
  No harm done, but wasted work
Caller-save
  What if main() doesn't use r1-r4?
  No harm done, but wasted work
void foo(){
int a,b,c,d;
a = 5; b = 6;
c = a+1; d=c-1;
save r1 to stack save r4 to stack
bar();
restore r1
restore r4
d = a+d;
return();
}
void foo(){
int a,b,c,d;
save r1
save r2
save r3
save r4
a = 5; b = 6;
c = a+1; d=c-1;
bar();
d = a+d;
restore r1
restore r2
restore r3
restore r4
return();
}

## Slide 34: Another helpful visual
foo() {
. . .
bar ();
. . .
}
bar() {
. . .
. . .
. . .
}
Caller save
Caller restore
Callee save
Callee restore
CALLER-CALLEE
Notes: 34

## Slide 35: Saving/Restoring Optimizations
Where can we avoid loads/stores?
Caller-saved
  Only needs saving if value is “live” across function call
  Live = contains a useful value: Assign value before function call, use that value after the function call
  In a leaf function (a function that calls no other function), caller saves can be used without saving/restoring
CALLER-CALLEE
void foo(){
int a,b,c,d;
a = 5; b = 6;
c = a+1; d=c-1;
bar();
d = a+d;
return();
}
a, d are live
b, c are NOT live
Notes: 35

## Slide 36: Saving/Restoring Optimizations
Where can we avoid loads/stores?
Callee-saved
  Only needs saving at beginning of function and restoring at end of function
  Only save/restore it if function overwrites the register
CALLER-CALLEE
void foo(){
int a,b,c,d;
a = 5; b = 6;
c = a+1; d=c-1;
bar();
d = a+d;
return();
}
Only use r1-r4
No need to save other registers
Notes: 36

## Slide 37: Caller versus Callee
Which is better??
Neither is obviously better – depends on specific code
Common solution: designate some registers as caller-saved, some as callee-saved
More next time

## Slide 38: Next Time
Finish Up Function Calls
Talks about linking – the final puzzle piece of software
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah
Live Poll + Q&A: slido.com #eecs370