## Slide 1: EECS 370 - Lecture 8
Combinational Logic
Live Poll + Q&A: slido.com #eecs370
Poll and Q&A Link

## Slide 2: Announcements

## Slide 3: Floating Point Arithmetic
See end of slides for bonus material (not covered in HW or exams)

## Slide 4: Why floating point
Have to represent real numbers somehow
Rational numbers
  Ok, but can be cumbersome to work with
Fixed point
  Do everything in thousandths (or millionths, etc.)
  Not always easy to pick the right units
  Different scaling factors for different stages of computation
Scientific notation: this is good!
  Exponential notation allows HUGE dynamic range
  Constant (approximately) relative precision across the whole range

## Slide 5: IEEE Floating point format (single precision)
Sign bit: (0 is positive, 1 is negative)
Significand: (also called the mantissa; stores the 23 most significant bits after the decimal point)
Exponent: used biased base 127 encoding
  Add 127 to the value of the exponent to encode:
  -127  00000000 1  10000000
  -126  00000001 2  10000001
  … …
  0  01111111 128  11111111
How do you represent zero ? Special convention:
  Exponent: -127 (all zeroes ), Significand 0 (all zeroes), Sign + or -
Some other exception cases (e.g. NaN) we won't cover

## Slide 6: Floating Point Representation
10.625 10
1010.101 2
Step 1: convert from decimal to binary
  1st bit after "binary" point represents 0.5 (i.e. 2-1)
  2nd bit represents 0.25 (i.e. 2-2)
  etc.

## Slide 7: Floating Point Representation
10.625 10
1010.101 2
1.010101  2 3
Step 2: normalize number by shifting binary point until you get 1.XXX * 2Y

## Slide 8: Floating Point Representation
10.625 10
1010.101 2
1.010101  2 3
Significand (1010101)
Exponent (3)
+/-
1 bit
23 bits
8 bits
This must be a 1!
So don’t store it.
Step 3: store relevant numbers in proper location (ignoring initial 1 of significand)

## Slide 9: Floating Point Representation
10.625 10
1010.101 2
1.010101  2 3
This must be a 1!
So don’t store it.
10.62510 = 0 10000010 01010100000000000000000
Significand (1010101)
Exponent (3)
+/-
1 bit
23 bits
8 bits

## Slide 10: Class Problem
What is the value of the following IEEE 754 floating point encoded number?
1
10000101
01011001000000000000000
10
Poll
1 = -
10000101 = 133 – 127 -> exponent 6
01011001 = mantissa
-1.01011001 x 2^6
-1010110.01
-(2^6+2^4+2^2+2^1+2^-2)
-(64+16+4+2+1/4)
-86.25
Notes: 1 = -
10000101 = 133 – 127 -> exponent 6
01011001 = mantissa
-1.01011001 x 2^6
-1010110.01
-(2^6+2^4+2^2+2^1+2^-2)
-(64+16+4+2+1/4)
-86.25

## Slide 11: What matters to a CS person?
When you are adding small numbers to big numbers, the result may not change
  E.g. 1.00 x 103 + 1.00 x 101 = 1000+1=1.00x103
This can be a real problem when writing scientific code.
  For the above example, imagine you did that addition a million times
  You’d still have 1000 when the answer should be 1,001,000
So you need to be aware of the issue.
  This is why most people use “double” instead of “float”
  The problem can still exist, it’s just less likely.

## Slide 12: More precision and range
We've described IEEE-754 binary32 floating point format, i.e. “single precision” (“float” in C/C++)
  24 bits precision; equivalent to about 7 decimal digits
  3.4 * 1038 maximum value
  Good enough for most but not all calculations
IEEE-754 also defines larger binary64 format, “double precision” (“double” in C/C++)
  53 bits precision, equivalent to about 16 decimal digits
  1.8 * 10308 maximum value
  Most accurate physical values currently known only to about 47 bits precision, about 14 decimal digits

## Slide 13: Single (“float”) precision
8

## Slide 14: Next few lectures: Digital Logic
Lectures 1-7:
  LC2K and ARMv8/LEGv8 ISAs
  Converting C to Assembly
  Function Calls
  Linking
Today:
  Floating Point
  Combinational Logic
Next lecture:
  Sequential Logic

## Slide 15: Up Until Now…
We’ve covered high-level C code to an executable
  Compilation
  Assembly
  Linking
  Loading
Now, we’ll talk about the hardware that runs this code
  First step: the basics of digital logic

## Slide 16: Next 3 Lectures
Combinational Logic:
  Basics of electronics; logic gates, muxes, decoders
Sequential Logic
  Clocks, latches and flip-flops
State Machines
  Building a simple processor

## Slide 17: Transistors
At the heart of digital logic is the transistor
Electrical engineers draw it like this
The physics is complicated, but at the end of the day, all it is a really small and really fast electric switch
High voltage here makes transistor act like a wire*
*Yeah, yeah, circuits people. It's a lot more complicated than that. This abstraction is fine for 370.
Low voltage here makes transistor act like an open switch*
1
0
We use 1 to represent HIGH voltage, 0 to represent LOW voltage

## Slide 18: Basic gate: Inverter
I
O
0
1
1
0
I
O
Truth Table
CS abstraction - logic function
Schematic symbol (CS/EE)
We won't focus on this part in 370. Take 270 and 312 to learn more

## Slide 19: Basic gates: AND and OR
AND
OR
A
B
0
0
1
1
0
1
0
1
0
0
0
1
Y
A
B
Y
Truth Table
A
B
0
0
1
1
0
1
0
1
0
1
1
1
Y
A
B
Y
Truth Table

## Slide 20: Basic gate: NAND
A
B
0
0
1
1
0
1
0
1
1
1
1
0
Y
A
B
Y
Truth Table
Transistor-level schematic
Layout schematic
Take 427 to learn more (sooooo many rectangles in that class)
Bubble is symbolic for "invert", so this is equivalent to negating an AND gate

## Slide 21: Basic gate: XOR (eXclusive OR)
A
B
0
0
1
1
0
1
0
1
0
1
1
0
Y
A
B
Y
Truth Table
Poll: How do we fill in the truth table for XOR? XNOR?
A
B
Y
XNOR Gate
Live Poll + Q&A: slido.com #eecs370

## Slide 22: Building Complexity: Selecting
We want to design a circuit that can select between two inputs (multiplexer or mux)
Let’s do a one-bit version
  Draw a truth table
A
B
0
0
0
0
0
0
1
1
0
1
0
1
S
O
1
1
1
1
0
0
1
1
0
1
0
1
Symbol
Poll: How do we fill in the truth table for this?
O
O = S ? B : A
Live Poll + Q&A: slido.com #eecs370

## Slide 23: Building Complexity: Selecting
We want to design a circuit that can select between two inputs (multiplexor or mux)
Let’s do a one-bit version
  Draw a truth table
A
B
0
0
0
0
0
0
1
1
0
1
0
1
S
O
1
1
1
1
0
0
1
1
0
1
0
1
Symbol
O
O = S ? B : A
0
0
0
1
1
0
1
1
A
S
B
C
Circuit
Is A if S is 0
Is 0 if S is 1
Is 0 if S is 0
Is B if S is 1
Is A if S is 0
Is B if S is 1
Muxes are universal! A 2N entry truth table can be implemented by passing each ouput value into an input of a 2N–to-1 mux

## Slide 24: Building Complexity: Addition
We want to design a circuit that performs binary addition
Let’s start by adding two bits
  Design a circuit that takes two bits (A and B) as input
    Generates a sum and carry bit (S and C)
  Make a truth table
  Design a circuit
1 0 0 1 1
+ 0 0 1 1 0
A
B
C
S

## Slide 25: Building Complexity: Addition
S
We want to design a circuit that performs binary addition
Let’s start by adding two bits
  Design a circuit that takes two bits (A and B) as input
    Generates a sum and carry bit (S and C)
  Make a truth table
  Design a circuit
1 0 0 1 1
+ 0 0 1 1 0
1 1 0 0 1
0 1 1 0
A
B
C
C
S
A
B
0
0
1
1
0
1
0
1
0
0
0
1
0
1
1
0

## Slide 26: Building Complexity: Addition
Now we can add two bits, but how do we deal with carry bits?
This is a full adder
  We have to design a circuit that can add three bits
    Inputs: A, B, Cin
    Outputs: S, Cout
  Design a truth table
  Circuit
This is a full adder
1 0 0 1 1
+ 0 0 1 1 0
1 1 0 0 1
0 1 1 0
Cin
A
0
0
0
0
0
0
1
1
0
1
0
1
B
0
1
1
0
S
0
0
0
1
Cout
1
1
1
1
0
0
1
1
0
1
0
1
1
0
0
1
0
1
1
1
A B Cin
S
Cout

## Slide 27: 8-bit Ripple Carry Adder
Full
adder
C
A7 B7
A6 B6
A5 B5
A4 B4
A3 B3
A2 B2
A1 B1
A0 B0
Full
adder
Full
adder
Full
adder
Full
adder
Full
adder
Full
adder
Full
adder
S7
S2
S1
S0
S6
S5
S4
S3
Carry
This will be very slow for 32 or 64 bit adds, but is sufficient for our needs
If we invert B's bits and set C to 1, we also have a subtractor! Why?

## Slide 28: Building Complexity: Decoding
Another common device is a decoder
  Input: N-bit binary number
  Output: 2N bits, exactly one of which will be high
  Allows us to index into things (like a register file)
Decoder
A0
A1
Out0
Out1
Out2
Out3
Poll: What will be the output for 101?
Live Poll + Q&A: slido.com #eecs370

## Slide 29: Propagation delay in combinational gates
Gate outputs do not change exactly when inputs do.
  Transmission time over wires (~speed of light)
  Saturation time to make transistor gate switch
  ⇒ Every combinatorial circuit has a propagation delay (time between input and output stabilization)
I
O
O
I
Vdd
gnd
Vdd
gnd

## Slide 30: Timing in Combinational Circuits
A
S
B
C
MUX
X
Y
A
S
B
X
Y
C
dG2
G1
G2
G3
dG3
dG2
dG3
What is the input/output delay (or simply, delay) of the MUX?
Delay of gate G2
time

## Slide 31: What is the delay of this Circuit?
3
5
2
6
1
A
B
C
D
E
F
Each oval represents one gate, the type does not matter
Poll : What is the delay?
We only care about the longest path, or critical path
Live Poll + Q&A: slido.com #eecs370

## Slide 32: Exercise
Use the blocks we have learned about so far (full adder, NOR, mux) to build this circuit
  Input A, 32 bits
  Input B, 32 bits
  Input S, 1 bit
  Output, 32 bits
  When S is low, the output is A+B, when S is high, the output is NOR(a,b)
Hint: you can express multi-bit gates like this:
32
32
32
Full
Adder
Circuit
32
32
32

## Slide 33: Exercise
This is a basic ALU (Arithmetic Logic Unit)
It is the heart of a computer processor!
Full
Adder
Circuit
32
32
A
B
S
0
1
32
output

## Slide 34: Next Time
Logic circuits that "remember"
  Aka "sequential logic"
Lingering questions / feedback? I'll include an anonymous form at the end of every lecture: https://bit.ly/3oXr4Ah
Live Poll + Q&A: slido.com #eecs370

## Slide 35: BONUS Floating Point Slides

## Slide 36: Bonus slides – this material is not testable
This material is here for those folks that may care.
  You may find it useful when considering the gap between representations
  But the material isn’t directly testable.
It is interesting if you are into that kind of thing.
It can be useful if you are going to do scientific programming for a living.
So it is provided as a reference, but isn’t part of the class (we may cover a bit of it in lecture if we have time)
Not testable

## Slide 37: Floating point multiplication
Add exponents (don’t forget to account for the bias of 127)
Multiply significands (don’t forget the implicit 1 bits)
Renormalize if necessary
Compute sign bit (simple exclusive-or)
Not testable

## Slide 38: Floating point multiply
0 10000010 01010100000000000000000
10.625 10 = 1010.1012
10 10 = 10102
0 10000010 01000000000000000000000
1 0 1 0 1 0 1
 1 0 1
1 0 1 0 1 0 1
1 0 1 0 1 0 1 0 0
1 1 0 1 0 1 0 0 1
0 10000101 10101001000000000000000

1101010.012
= 106.2510
+
-127
38
EECS 370: Introduction to Computer Organization
Not testable

## Slide 39: Floating point addition
More complicated than floating point multiplication!
If exponents are unequal, must shift the significand of the smaller number to the right to align the corresponding place values
Once numbers are aligned, simple addition (could be subtraction, if one of the numbers is negative)
Renormalize (which could be messy if the numbers had opposite signs; for example, consider addition of +1.5000 and – 1.4999)
Added complication: rounding to the correct number of bits to store could denormalize the number, and require one more step
Not testable

## Slide 40: Floating point Addition
Shift smaller exponent right to match larger.
Add significands
Normalize and update exponent
Check for “out of range”
40
EECS 370: Introduction to Computer Organization
Not testable

## Slide 41: Class Problem
Show how to add the following 2 numbers using IEEE
floating point addition: 101.125 + 13.75
41
EECS 370: Introduction to Computer Organization
Not testable

## Slide 42: Class Problem
0
10000101
10010100100000000000000
0
10000010
10111000000000000000000
Shift mantissa by difference in exponent
00110111000000000000000
101.125
13.75
Sum Significands
1 1 0 0 1 0 1 0 0 1
+ 0 0 0 1 1 0 1 1 1 0
1 1 1 0 0 1 0 1 1 1
Note: When shifting to the right, the first shift should put the implicit 1, then 0’s
0
10000101
1100101110000000000000
= 114.875
Shift by 6-3 = 3
Sum didn’t overflow, so no re-normalization needed
Not testable

## Slide 43: Class Problem
Show how to add the following 2 numbers using IEEE
floating point addition: 117.125 + 13.75
43
EECS 370: Introduction to Computer Organization
Not testable

## Slide 44: Class Problem
0
10000101
11010100100000000000000
0
10000010
10111000000000000000000
Shift mantissa by difference in exponent
00110111000000000000000
117.125
13.75
Sum Significands
1 1 1 0 1 0 1 0 0 1
+ 0 0 0 1 1 0 1 1 1 0
1 0 0 0 0 0 1 0 1 1 1
Note: When shifting to the right, the first shift should put the implicit 1, then 0’s
0
10000110
0000010111000000000000
= 130.875
Shift by 6-3 = 3
Sum overflows, re-normalize by adding one to exponent and shifting mantissa by one
Not testable